INITIAL SETUP FOR DIGIPROM MB-XA 64.
  """"""""""""""""""""""""""""""""""""
 
  If you have a Printer it is suggested that you print this file to paper
  to make the SETUP procedure a lot easier and quicker to follow. If you
  dont know how to Print from Digiprom, then copy this file from your Main
  Disk to your Working disk and use the Word processor to print it out.
 
  Read all of this paragraph before following the instructions it
  contains. If you dont Have a File Copying programme, leave your Working
  Disk in the drive and suitch off the computer for 5 seconds and then
  switch back ON again and type LOAD"*",8,1 and press return. This will
  load in the menu. Select 3 to enter the Word Processor. Take your Working
  Disk out of the drive and replace it with the MAIN DISK. Press F6
  followed by F1 and type in HELP FILE and press return.
  When loaded remove the Main Disk and replace it with the Work Disk and
  press F6 followed by F5 and type O and press return.
  Again remove the Work Disk and replace it with the Main Disk and press F6
  followed by F1 and type SETUP (return). When the file has loaded, remove
  the MAIN DISK from the drive and insert your Working Disk. Now press F6
  followed by F5 and type SETUP (return). This will save the SETUP File to
  your working disk. If you dont have a Printer it will mean you will have
  to Read this file from within Digiprom several times. ie: Type END to
  enter the main Menu, and then press 1 to enter The Digiprom MB-XA 64
  programme. When loaded type :V SETUP (return). Use the Space Bar to pause
  when some instructions are shown on screen and then press the RUN/STOP
  key to enter programming mode. Enter the commands or alterations as
  instructed and when finished, type :V SETUP (return). This will start the
  SETUP file from the beginning again, so use the Space Bar to pause at the
  point of the next set of instructions. Holding down the CONTROL key will
  slow down the scrolling speed of the file and make it easier for you to
  find the exact place you were last at. Continue in this fashion until you
  have read and made all the alterations as instructed. The XA MANUAL 1 to
  8 files can be read in the same manner. Dont copy the 8 manual files to
  your work disk because it will almost fill the disk leaving very little
  room for msgs and the like.
 
 When instructed to type something in following a direct Cmd, such as the
  cmd :MYcall, use lower case letters only. Use capital letters only when
  changing text such as that in the ST memories.
 
  Type :Clock (Time), type in the time as per 24 hour format. ie 1640 and
  press return. This has to be done each time the programme is booted up.
  The time forms part of the operating system so MUST BE SET.
 
  Now for the date. Type :DA 19 9 99 or whatever the date is, and press
  return. This also forms part of the operating system and MUST BE SET.
 
  To enter your callsign in port 1 type :MY (callsign)(return). Press and
  hold down the Commodore logo Key, and press number 2. (Not F2). This
  will put you in port 2. Type :MY (callsign)-2(return). You dont have to
  use a SSID if you dont want to. (This will be your Mail Box Port.) Again,
  hold down the Commodore Logo key, and at the same time press number 3.
  Now type :MY (callsign)-8(return) to enter your Node callsign. Your Node
  ALIAS can be typed in from any port and it will automatically be placed
  in port 4. An ALIAS usually takes the form of your local Town name. eg: I
  live in a town named Billingham, so I use BIL21 as my ALIAS. The numbers
  signify which frequency is used. ie: 21 for 144.650 and 22 for 144.675.
  etc. To enter your Alias type :ALIAS (your alias)(return).
 
  Now hold down the Logo key and press 1 to get back to Port 1.
 
  With your Working Disk in the Drive, type :SA (return) to save your
  callsign alterations to disk as PRMTXA 0.
 
  Now type :BT(return) to display your Beacon Text, and replace the XXXXX
  with your callsign. Also, type in your Alias over the word ALIAS. At
  TOWN and COUNTY type in your Town and County. (Use Capital Letters).
  When finished press return.
 
  Type :A (return) to display your Answer Text and type your local BBS
  callsign over the top of the GB7XXX. Delete any excess Xs and close up
  spaces with the DEL key. The finished parameter should be similar to
  this, :A GB7UWS:C, XXXXX:D, XXXXX:D, XXXXX:D. When finished press
  return. This parameter will allow your local BBS to download personal
  mail direct to your disk. (Subject to you asking your local BBS Sysop to
  do this for you.) Again, type :S (return) to save the changes to disk.
  :S is the abbreviation for the :SAVEP (Save Parameters) command.
 
  Type :BBS (return) and enter your callsign over the Xs. (Use SHIFT and
  INST/DEL to widen the gap if your callsign is longer than 5 digits. Use
  DEL to shorten gap if less than 5 digits.)
 
  Type your local BBS callsign over the Zs and the Number of your Local
  BBS over the YY. (If you dont know this number then connect to your
  local BBS Sysop and ask him/her.) Do not attempt to use this programme
  until the YY number is in place.
 
  Type in your home Town and County over the TOWNTOWN,COUNTYCOUNTY
  shortening or lengthening as neccessary using the keys already
  mentioned. The # and all other punctuation marks plus brackets must
  remain. Do not add to, or delete any of them. They form part of the
  operating system. Press return when completed.
 
  Type :MFWD (return) and type your Local BBS callsign over the first
  callsign in the row, then press return. (The other *Xs are explained in
  the XA manual under :MFWD.)
 
  Type :SA (return) to save changes to disk.
 
  For Non UK Users type :TPUK OFF (return). This will allow your station
  to receive Third Party Mail. Dont forget to :S (return).
 
  For Non UK Users operating from a mains frequency of 60Hz (cycles) you
  will need to type :FRQ ON (return). Again :S (return) to save it.
  NOTE: Non UK users operating on 60Hz Mains Frequency who experience
  difficulty with TX and RX while using 1200 Baud should reduce their
  BAUD Rate setting to 1145. ie  :HBAUD 1145 (return). Dont forget to save
  this alteration to disk with  :S (return).
 
  This completes the initial setup and your station is now ready to TX &
  RX Packet Data and to Auto Forward Mail or Bulletins to your Local BBS.
  (Provided of course that you are able to connect to it.)
 
  NOTES: To alter the colour of the text and background type :COLOUR # #
  where # # can be any two numbers from 0 to 15. Likewise, to alter the
  border colour to match the background type :BCOLOUR # where again the #
  is any number from 0 to 15. These numbers and the colours obtained from
  them are given in detail in your 64 computers handbook. (or 128
  handbook). Default is :COLOUR 0 7 and :BCOLOUR 0.
 
  :SP Call @ BBS:Subject (return) Is for Auto Forwarding or for attaching
  to your MAIL FOR BEACON, so it is essential that you read the XA MANUAL
  before using :SP. (Only use Lower Case letters for entering callsigns
  and Subject.) YOU HAVE BEEN WARNED!!
 
  Digiprom MB-XA 64 contains a routine which checks the system every 60
  seconds. This will only be noticed on such things as the SD window
  which, provided you have just written a msg for forwarding, will go into
  reverse video only after the system has been checked. Also, the F5
  JHEARD screen will contain garbage on Fire Up which will clear to the
  normal screen after the system check, or when new stations are heard.
  You will probably have already experienced the 60 second delay (Magic
  Minute as we refer to it) when you entered the Date.
  To get the full benefits from Digiprom MB-XA it is recommended that you
  read the full instructions which can be found in the XA Manuals. These
  manuals are on the MAIN DISK in 8 parts, being XA MANUAL 1 to 8.
 
  For those needing extra help with the Word processor a small file can be
  found on the MAIN DISK. The file is named WORD PROC.
 
  Finally, set the volume and squelch on your radio to approximately the
  1'oclock positions.

 
                   COPYRIGHT (C) JSM GROUP 1992.
 MB-XA 64 is the first version of a completely new style of Packet
  Software written exclusively for the Commodore 64  series computers.
  Its many features include Ease of Use, Auto Forwarding of Messages and
  Bulletins to your local BBS or to any other MB-XA128 or MB-XA64 station
  that you can connect to either direct, or via a Node Path. All of the
  Parameters, apart from those mentioned in the SETUP File, are pre-set
  for optimum performance.
 
  MB-XA will automatically switch to BBS Mode on reception of a BBS Cmd,
  or when Auto Forwarding. At all other times the software is used as a
  normal PBBS.
 
  MB-XA contains three independent routines for continually checking the
  system. These consist of a check every 60 seconds (Magic Minute) to
  update the system to any cmds that you may have entered, such as :DATE
  where the date will take a Magic Minute before changing, (you can
  override the delay on date fixing by holding down the CONTROL key and
  pressing 1 2 3 4 and 1.) or the :SP facility. This 60 second check will
  only be noticed as a delay between finishing a msg for forwarding, and
  the time it takes for the SD Box to light. (Go into reverse video.) Will
  also be noticed on the F5 Jheard screen. A 30 Minute check to see if
  there is any mail to be forwarded or added to your MAIL FOR Beacon, if
  any is found the system will enter BBS mode and start Auto Forwarding,
  or transmit a MAIL FOR beacon. The beacon will not be transmitted if you
  have no mail on your PBBS. The third routine comes into effect a few
  minutes after 2400 Hours (Midnight) and this will automatically kill off
  those messages which have been Auto Forwarded. (Provided the computer has
  not been switched off since the msgs were forwarded.) Should any msg fail
  to be Auto Forwarded after a period of 24 hours it must be manually
  killed by use of the :K cmd, this will ensure the correct assignment of
  BID Numbers.
 
  The highest Msg number allowed by this system is 255, but you should
  always keep in mind that the maximum number of files that can be stored
  on a disk via a Commodore Disk Drive is only 140, regardless of file
  type or size.
 
  Digiprom MB-XA is issued on a MAIN DISK which must be used for creating
  a Work Disk. Do not remove the Write Protect Tab from the MAIN DISK.
  If you want to make a copy of the MAIN DISK you must use a Disk Copy
  Programme. The XA MANUAL, SETUP, WORD PROC and INFO files can be copied
  using a File Copier, but not the Programme file.
 
  With the computer switched OFF insert the MAIN DISK and turn the drive
  ON. Then switch on the computer and follow on screen instructions
  exactly as stated. IMPORTANT: YOU MUST READ THE SETUP FILE.
 
  It takes between 3 to 7 minutes to create the Work Disk which will auto
  boot into the main menu.
 
  1 will take you directly into the Digiprom programme.
  2 to enter the PMS SORT-RENUMBER. This will quite literally Sort and
  Re-number your Msg file. Be prepared for a long wait while this routine
  sets about its business. NOTE: Apart from Killing all your msgs manually
  this is the only way to ensure that your msg numbers dont go too high.
  3 to enter the Word Processor. Press the HELP key for info on the cmds,
  and if you need more help read the WORD PROC file.
  4 to enter the file conversion routines. This will allow you to convert
  a programme file into a sequential file so that it can be transmitted to
  another station via a Node. (Nodes have a nasty habit of stripping the
  last BIT (8) from an 8 BIT programme.) Use the :WPRG Cmd to send a
  programme file to another station that you can connect to direct.
  Sequential files (Msgs etc) can also converted into a non readable code
  for transmission over air, but the recipient must be a Digiprom user to
  be able to convert it back to readable text.
  NOTE: Conversion of any file will physically double its size. ie: 5K
  normal = 10K converted.
 
  The Work Disk will contain the following files:
  M1. M2. M3. These are the programme files. PRMTXA 0 is your parameter
  file. PRMTXA # is the message management file. U is the file where all
  incoming mail is stored.
 
  It is important to note that Digiprom MB-XA was written for use with the
  Commodore printers, 801, 802, 803 and the 1101, and while some non
  Commodore printers may work, others might not.
 
  ALL VERSIONS OF DIGIPROM.
  If you are using a monitor with sound you should hear two distinct
  tones. These tones will always sound when somebody connects to you or on
  a disconnection. (Very handy if you are the other side of the shack
  pounding away on your PC.)
 
  DIGIPROM MB-XA 64 PACKET SCREEN.
  The Clock prompt will be flashing, type in the time like this leaving no
  spaces, 1845 or whatever the time may be, and press return. The time
  will appear at the far right of the lower status line after CLOCK.
 
  With the colon (:) at the start of the next line type :DA 13 7 92 or
  whatever the date may be, not forgetting the return. The DAte will be
  displayed in the top status line to the far right. (After the Magic
  Minute system check.)
 
  Read the SETUP file for information on how to insert your parameters.
 
  The top status line begins with PORT square spacer and a reverse video
  square with number 1 in it. This obviously shows you are in port 1.
  Press CONTROL and 2 and the number will change to 2 showing that you are
  now in port 2. (Mail Box port). Press CONTROL and 1 to go back to port 1.
 
  The next square is a spacer followed by CALL another spacer and then
  your callsign. (If entered.) Another square spacer is followed by the
  DIGIPROM VERSION, another spacer and then RX. The box next to this will
  light (go into reverse video) when a station has left you a msg in your
  mail box. When you have read the msg with the :V cmd (remembering the 60
  second system check) the box will revert to a normal square.
 
  The next square is a spacer followed by SD and another box. This box
  will light (reverse video) whenever there is mail waiting to be auto
  forwarded. Again, it will revert back to a normal box when the data has
  been forwarded. (Subject to the magic minute check.)
  Date has already been explained. The remaing square boxes are spacers.
 
  Lower Status Line. The box following PTT will light (reverse video) each
  time your station transmits. The box following STA will light (reverse
  video) when data is in the computers buffer waiting to transmit. The box
  after DCD will flash on or off as data is detected. The box following
  PATH will light (reverse video) if you have mail to forward via your
  Node Path, or you are using your path to connect to another station. The
  next square is a spacer.
 
  The JSM GROUP LOGO box will change to LINK MADE WITH callsign each time
  you make a connect or a connect is made to you. The next square is a
  spacer. CON is followed by 4 boxes which represent the 4 ports. ie: If a
  station CONnects on port 2 then box 2 will light. (reverse video.)
  CLOCK has already been explained. The remaining two squares are spacers.
 
  Should a station attempt to connect to a port that you are already using
  the top left of the top status line will change to CONNECT REQUEST and
  the callsign of the station calling. A tone will also sound if your
  monitor is equiped for sound. This will remain for the magic minute
  system check before reverting back to the normal status line.
 
  The callsign of the last station that was connected to you will be
  displayed on the left top side of the TX screen together with the time
  of disconnection.
 
  Between the two status lines is the TX screen. Below the lower status
  line is the RX screen.
 
  IMPORTANT NOTES. The :ST memories form part of the operating system.
  The deletion or changing of any of the reverse video Control tokens, or
  indeed any of the text will cause a malfunction of the software.
 
  When you connect to another station, that station will not be able to
  send remote commands of any kind. Only the station making the original
  connect can send remote commands. This routine has been written in to
  prevent false operation of commands used for BBS forwarding etc.
 
  When using the :SP facility, all cmds must be entered in Lower case.
  NOTE: The :SP facility in the 64 version is totally different from the
  128 version so it is important to read the instructions on :SP in this
  manual.

  Between the status lines is the TX area. Below the lower status line is
  obviously the RX screen.
 
  The lower status line is set at 8 but this can be changed to suit your
  own needs. The cmd is :DIV 12 to lower the status line to 12. :DIV 15
  for for line 15 etc. The maximum for the DIVision line is 22. Div is a
  parameter which has been set at 8 for a very gomd reason. ie: If RX data
  should come in fast, it will scroll off the top of the screen and cannot
  be recovered. It can of course be saved to disk, but more on that
  further into this manual.
 
  Notice that the date is on the far right of the top status line and the
  time is shown at the far right of the lower status line.
 
  The 4 ports are: Port 1 your callsign. Port 2 your callsign-2. You dont
  have to use a -2 SSID if you prefer not to. (This is your Mail Box Port.)
  Port 3 your callsign-8 for your Node. Port 4 your Node Alias. It is worth
  remembering that any Digiprom port can be used for receiving mail, so if
  you are in connection on port 1 and another station connects to any other
  port they can easily leave a msg for you. As said, Port 3 is callsign-8.
  Port 4 is the Alias for your Lode. Details of how to enter your Alias can
  be found further on, and in the SETUP file. NOTE: The maximum callsign
  allowed is 8 digits including a SSID. Callsigns beginning with a number
  are accepted in MB-XA.
 
  The ports are accessed by pressine and holding down the CONTROL or CBM
  Logo key and pressing 1 for port 1, 2 for port 2 etc.
 
  With your radio switched OFF, press CONTROL and 2. The port status will
  show that you are now in port 2. Type :MY G9ABC(return) followed by :C
  (your callsign)(return.) The RX screen will show you what a connecting
  station would receive if he/she logged onto your port 1. You will also
  notice that the cmd colon (:) has gone. You dont use the colon (:) when
  connected to another station. The callsign mf the connecting station
  will be shown in the middle of the lower status line.
 
  For a brief explanation of what the commands on screen actually do, I
  suggest pressing the H key. Then, as with most BBSs, use the ? with the
  cmd that you want infopmation on. Disconnect with the Bye cmd, and dont
  forget to put your own callsign back in port 2 with the cmd :MY (your
  callsign)(-2 SSID if wanted)(return).
 
  The cmd line beginning with your callsign shows all the cmds available
  to the station connected to you.
 
  They are: B,H(Help),I,KM,L,LM,R,SP,V,WS,?
 
  Very briefly these are B Bye = Disconnect. H(Help) will call a help
  file from disk. (O file.) I calls the Station INFO file from disk. (M
  file.) J shows your stations Heard list. KM Kill Mine is used"by
  connected station to kill off any msgs that you may have written for
  him/her. L List will show any msgs addressed to ALL or for the station
  connected to you. LM List Mine will list any msgs that you have written
  for the connected station. If no msgs are found then the connected


  3 of MB-XA INSTRUCTIONS.   Copyright (C) JSM GROUP 1992.
    """"""""""""""""""""""""""""""""""""""""""""""""""""""""
 
  You will notice that some of the RCMD parameters already have a 0 switch
  appended to them. They should be left as they are, otherwise a
  connecting station  will be unable to leave msgs, do a List or even
  disconnect from you.
 
  And now for a look at the ST (Send Text.) this is the text that is
  either transmitted to a station connecting to you, or is sent in answer
  to a specific command or commands. To view it type :DIV 22(return) to
  lower the bottom status line, (not forgetting to type :DIV 8 (return)
  when you have finished viewing) then type :SList (return) or simply :SL
  (return). All the text following the A is that which is transmitted when
  a station connects to your port 1 or port 2.
  All of the text and reverse video tokens form part of the operating
  system. DO NOT ALTER ANYTHING IN THE ST MEMORIES. YOU HAVE BEEN WARNED!
 
  If you would like to see how your Send Text is received by a connecting
  station, then follow this procedure. Type :XM OFF (return). This will
  switch off the transmitting routine in the programme so that nothing
  will go out over air. Press CTRL and number 3 to enter port 3. From port
  3 type :C (your callsign)(return) and all will be revealed. You can also
  practice your Packet skills by sending a few cmds to see what actually
  happens, and to find out what a connected station would receive. Dont
  forget to log off with a B (return) and CONTROL and 1 to get back to
  port 1.
 
  PARAMETERS.
 
  (Capital letters denote the abbreviation which should be used instead of
  the full parameter word.)
 
  :Atext.  (Local BBS callsign):C
  If your local BBS sysop has agreed to auto forward your personal mail to
  your disk drive, then set :Atext to (BBS callsign):C. This is set as
  default.
  For other MB-XA users who can connect to you enter their callsign
  followed by a D ie: G1SFK:D   Each callsign must be separated by a comma
  and a space.
 
  :ALIAS. (Your Node alias). This cmd allows you to use an alias with the
  Node in port 4. Typing :ALIAS (your alias) from any port will
  automatically place the alias in port 4. An Alias is nothing more than 3
  or 4 letters taken from your name or from the name of your town or
  county with a number added to signify frequency. ie: EDN21 = Edinburgh
  on 144.650Mhz. There is no need to use a number, in fact many Nodes just
  show a name such as CLEVE for Cleveland, or RUTLND for RUTLAND. (Maximum
  of 8 characters including a SSID.)
 
  :SLine. Typing :SL (return) will display part of the Send Text (ST) to
  the TX area of the screen. Press return to continue viewing. (Best to
  type :DIV 22 (return) before :SL. This will open up the TX area to 22
  lines and so make the viewing easier.)
  As already mentioned, most of the text and all of the reverse video
  Control Tokens form part of the operating system, so leave well alone
  until you are familiar with each function. Dont forget to type :DIV 8
  (return) to get back to the normal screen.
 
  The reverse video n (CTRL and RETURN) denotes a carriage return with
  line feed.
 
  Reverse video A (CTRL and A) stores the callsign of the station
  connected to you and re-transmits it as the full callsign.
 
  Reverse video C (CTRL and C) transmits your Node Alias/callsign in a
  similar fashion to that of THENET. eg:  WER21:G7AMW-8.
 
  Reverse video s sends the time and reverse video r sends the date.
 
  Reverse video E sends a stored programme msg to a connecting station if
  there is a msg for him/her on your PBBS. The msg informs him/her that
  they have Un-read mail.
 
  Reverse video D transmits your callsign.
 
  Reverse video P transmits the port number connected to.
 
  Reverse video B transmits a msg number.
 
  :AUto ##. Where ## is any two numbers from 11 to 78. This will set an
  automatic carriage return and line feed after ## number of characters
  have been typed. (Including spaces.) Word wrap is automatic. Default 78.
 
  :ACls ON or OFF. If ON will clear the screen on connect or disconnect.
  If another station has left you a msg on your disk the box next to RX on
  the top status line will be lit. (Reverse video.)
  If you have just downloaded a msg from your local BBS and have not saved
  it to disk, then make sure that :ACls is OFF, or the msg will be cleared
  from the screen. Default ON.
 
  :BAddress. What you type here is appended to your callsign and will be
  transmitted as part of your Beacon. Ideally you should have :BAddress
  ID, but if you want to call CQ then type :BAddress CQ. Default ID.
 
  :HBaud sets the Baud Rate. :HBaud 300 for HF and :HBaud 1200 for VH/UHF.
  Maximum setting is 2800. Default 1200. NOTE: Using a 60Hz mains freqency
  will require the 1200 rate to be reduced to about 1145.
 
  :BEacon Every/After ## sets the time loop for transmission of the BText
  (Beacon text) and is measured in 10 seconds multiplied by ##. eg:
  :BEacon E 180 will transmit the contents of BText (Beacon Text) every 30
  mins. :BEacon A 180 will transmit the beacon text After the frequency
  has been clear for 30 minutes. For no beacon, set :BEacon OFF. Do not
  set the beacon to transmit on less than a 30 minute cycle. You may like
  it but others wont. Default 500.
 
  :BColour # sets the border colour of the screen. # can be any number
  from 0 to 15. See your 64 manual for colours obtained by these numbers.
 
  :BText (text). What you type here, (maximum of 80 characters including
  spaces) is appended to your callsign plus :BAddress, and is transmitted
  as a Beacon at the interval of time chosen from :BEacon Every/After ##.
  The text can be transmitted on several lines by the inclusion of CTRL
  and M at several points within the text. For example: :BT(CTRL M)
  DIGIPROM(CTRL M)(Callsign-2 MBX(CTRL M)Callsign-8 NODE(CTRL M)(return).
  This would be seen on other stations monitors as:
 
    Callsign>ID>UI
    DIGIPROM
    Callsign-2 MBX
    Callsign-8 NODE
 
  Read the SETUP file for the default setting.
 
  Bye waits for packet data to be confirmed and then disconnects. This cmd
  is used without the colon (:) to end a connect to another station.
 
  :CAtalog will show a directory of your disk and print to screen the
  names of the programmes and or files that are on your disk together with
  the Block length and file type. Press the space bar to scroll through
  them if you have quite a few files on disk. (Pressing F2 will also
  perform the same function.)
 
  :CBell ON or OFF. If ON, a tone will sound on each connect or disconnect
  to or from your station. A tone will also sound if a connected station
  sends a T. default ON.
 
  :CFRom ALL or Callsigns. Use this if you only want connections from
  specific stations. eg: :CFRom G0001 G0002 G0003 (return) will only allow
  these three stations to connect to you. Any other station trying to
  connect will receive a BUSY FROM msg. Default :CFRom ALL.
 
  :CFilter (Characters or OFF.) This parameter set to OFF will pass some
  degree of remote control to a station who connects to your station. eg:
  If the connected station transmitted a CTRL R this would set your
  monitor to reverse video. (see Control Commands.) Default :CFilter
  ABCDEFHIJKLNOPQRSTUVWXY(|).
 
  :CLs (Direct Command.) If you have the parameter :ACLS OFF then you will
  need to clear your RX screen from time to time. Type :CLs (return) to
  perform this function.
 
  :CON (callsign). This is a connect command that is used to connect to a
  station that is in your Path list when you dont want to use the actual
  Path. eg: :PATH G9FOG,G9XYZ,G9ABC,G9DEF,G9TNT: Conditions are good with
  a bit of a lift on and you can hear G9ABC direct, so you would type :CON
  G9ABC (return). This would bypass the path routine and try for a direct
  connect. If the connect fails, just type :C G9ABC (return) to start the
  path going at G9FOG.
 
  :DNOT (callsigns or None). This is used to stop a named station or
  stations from using your station as a digipeater. eg :DNOT G9ABC will
  not allow G9ABC to digipeat via your station. Up to 5 callsigns can be
  used with this parameter, but each one must be separated by a comma.
  Default None.

  :CLOck (HHMM). You will need to set the time when the Digiprom MB-XA
  programme has been fired up. The :CLOCK prompt will automatically be
  shown just above the lower status line with the cursor flashing alongside
  it. Simply add the time in 24 hour format. eg: If you switch on at 1630
  then type 1630 at the cursor and press return. The clock will then be
  set with the current time and can be read from the right of the lower
  status line. Both the :CLOck and the :DAte will have to be set each time
  the software is fired up, or when you change the parameter file with the
  cmd :Getp. NOTE: The Time and Date form part of the operating system and
  must be set.
 
  :CMd ON or OFF. If ON, will insure that a colon (:) is placed in the
  first column of the next line when return has been pressed. The colon
  (:) is necessary for the parameters to work. On a connection being made
  to or from your station the CMd function is automatically switched OFF
  until a diconnection has been made. If you need to alter a parameter
  whilst connected you will have to type in the colon (:). Default ON.
 
  :CNot (callsigns or None). If you dont want a particular station or
  stations to connect to your station then type their callsigns here. eg
  :CNot G0000 G000A (return). If either of these stations attempt a
  connect to your station they will RX the BUSY FROM (your callsign). A
  maximum of 5 callsigns can be entered. Default NONE.
 
  :COLour A B. Where A can be any number between 0 to 15 and is the screen
  background colour. B can also be any number between 0 to 15 and is the
  text colour. See your 64/128 manual for explanation of the colour
  numbers. Default 0 7 (Green or Amber screen Monitor.)
 
  :CONOk ON or OFF. If OFF, then no station will be able to connect to
  you but you will still be able to connect to other stations. Default ON.
 
  :Connect (callsign). Used for initial connect to any station. For
  example :C G0000 (return) will transmit a connect request to that
  station, and if acknowledged, you will be connected. The : (colon) is
  not used for connecting to a second station via the digipeater or node
  of the station connected to. eg: Connect to the first station with :C
  (callsign), and when connected type C (callsign of the second station).
  The method of connecting to a second station is more efficient and uses
  less valuable air time if you first connect is to the Node of the
  station. Default Disconnected.
 
  :CText # or OFF. Where # is the text stored in ST for transmission on a
  given port when a station connects to you. For example: If you are in
  port 1 and you type :CT A (return) the text in ST A will be transmitted
  to the station who connects to that port. With :CT OFF (return) no
  connect text will be sent. Default on port 1 is :CT A. Port 2 is :CT A
  and Port 3 is :CT OFF. Port 4 is :CT B.
 
  :DAte (DD MM YY). Used for setting the date and is displayed in the top
  status line at the right hand corner of the screen. Each time the
  programme is fired up the date shown will be that when the disk was
  first copied, and of course will have to be reset. (Same as Clock.) To
  set the DAte type :DA 19 12 92 (return) or whatever the date may be. The
  date can be transmitted while connected by pressing SHIFT and +. The
  programme always assumes there to be 29 days in February. To alter the
  day only, type :DA (dd)(return) where dd is todays date. To alter the
  day and month only, type :DA (dd MM).
  NOTE: The date forms the BID numbers so must be set.
 
  :DIGi ON or OFF. When on, other stations can use your station as a
  digipeater. ie: A station can use your station as a repeater. The format
  used for this is :C (callsign) via (your callsign). Default ON.
 
  :DNot (callsign/s or None.) The callsign/s that you enter after :DNot
  will not be allowed to use your station as a repeater. A maximum of 5
  callsigns can be entered. Default NONE.
 
  :Disconnect. Forces an immediate disconnect from the station you are
  connected to. If you are connected to another station and the command
  Bye will not disconnect you, then use :D (return). Many of the Nodes
  currently in use will only accept the :D command, but dont use it until
  you see a msg on screen similar to FAILURE WITH (callsign), because the
  Node you are connected to may still be trying to make a connection for
  you. Default Disconnected.
 
  The Node used in Digiprom MB-XA is similar to THE NET Node. ie: if
  another station is using your node as a repeater and no connect is made,
  it will transmit the FAILURE WITH (callsign) msg. If you use your own
  node and no connect is made, the system will auto disconnect. In both
  cases, the system will return a FAILURE WITH (callsign) if a node is
  accessed which returns a connect text msg, (does not apply to KA Nodes)
  so only use those Nodes which have no connect text, such as THENET, KA
  or Digiprom, etc. Note: A station who is connected to your port 1 or 2
  will not be able to access your node at the same time.
 
  Digiprom MB-XA does not generate its own Nodes heard list. This will
  have to be compiled by you as the N file. (See the :WF Cmd further on.
  If you dont know what nodes your station can hear, then switch on your
  radio for an hour or so, and then press F5. All will be revealed.
 
  :DSelf ON or OFF. Used for test purposes. When ON will allow you to
  conneat to your own station via a digipeater. This is one method by
  which you can check that your station is functioning on both transmit
  and receive. Type :DSelf ON (return) followed by :C (your callsign) via
  (callsign of digipeater)(return). Default OFF.
 
  :DISPlay will show all your parameters with their settings to the top
  half of the screen, Press return to continue viewing, or SHIFT and
  RETURN to end. You can also change the parameter settings from this
  display by use of the cursor keys. Oake sure to press return on any
  parameter that you change. The use of SHIFT RETURN will also delete the
  colon (:) on the new line, so you will have to type it back again.
 
  :DTime #. Where # is a number between 10 and 255 which is then
  multiplief by 10 to give a time period in seconds. This will
  automatically disconnect you from another station if nothing is heard
  from the station after the time has elapsed. 0 (Zero) has no time limit,
  so if a station you are connected to should crash, 0 would cause your
  computer to hang indefinitely. default 90. (15 minutes.)
 
  :DIVision #. Where # is a number between 3 and 22 and represents screen
  lines above the lower Status line. Mainly used for viewing the Send Text
  and other settings such as :DISPlay, :RCMD etc. For example, type :DIV
  20 (return) and then type :SL (return). This will show approximately
  half of your Send text, and a single return will show the remainder.
  When you have finished viewing the text, dont forget :DIV 8 (return) to
  get back to the normal screen. Default is set at 8.
 
  :DWait #. Where # is a number between 4 and 255 and represents a time
  period of 40 milliseconds. This is multiplied by the numbers chosen and
  is the time that your digipeater will wait before transmitting. default
  10. (10x10 = .4 of a second.)
 
  :WFile (file-name) will allow you to write sequential files to disk in a
  similar fashion to the word processor, but it does have limitations.
  Type :WF (file name)(return) to prepare the disk for receiving a file,
  Delete the colon (:) next to the cursor and begin typing in your file or
  message. After typing several words or pressing return at the end of a
  sentence, the text will appear in the RX screen and at the same time
  will be written to disk. If you have made any spelling or other mistakes
  these too will be written to the disk. You cannot correct any errors
  once the text is in the RX portion of the screen. (If you do make
  spelling mistakes or any other error dont wopry too much because you cal
  always load the file into the word processor and correct the mistakes at
  a later date and re-save the file back to disk.) This applies to all
  versions of Digiprom. When you have finished writing the file make sure
  to gnd with a carriage return. Then type :WF OFF (return) to close the
  file and put the drive back to standby.
 
  There is no need to write a lengthy file in one go. You can add to it at
  any time by typing :WF (name of the file you want to add to) followed by
  an A. For example: If you had previously written a file called FRED and
  you want to add to it, type :WF FRED,A (return) and continue typing.
  Note: The text typed from the previous save will not be shown on screen,
  but I can assure you that whatever you type will be appended to FRED.
  You can add to a file as many vimes as you want to. (Subject to not
  running out of computer memory when you load the file back in from
  disk.) Default OFF.
 
  :EOf ON or OFF. If ON, will automatically pnace an "End of File" CTRL X
  at the end of any files or programmes that a connected station is
  reading from your disk. If set to OFF and you have files or programmes
  on disk that have no CTRL Z, and a connected station reads one of them
  and fails"to send a CTRL Z then your disk drive will remain in the open
  state, which will prevent other stations from either reading your disk,
  or leaving you a msg. Default OFF.

  /EX is used to end a message, sequential file or programme that you are
  transmitting to another station, CTRL Z can also be used. EXit, (typed
  as /EX) is a connected command and is used without the : colon.
 
  :FIle ON or OFF. If ON, a connected station who sends List or LM, (List
  Mine) will have access to your disk for reading or writing of messages.
  (Providing you have also set :RCMD FILE 0. See DISPlay already
  mentioned, and the :RCMD command which is further down this list.) If
  you dont use a disk drive then keep FIle OFF. Default ON.
 
  :FLdisk (disk command). This command allows the operator to use the DOS
  (Disk Operating System) to Scratch files etc. For example:
  :FL S0:(filename)(return) to scratch a file. :FL V(return) to Validate a
  disk. :FL N0:(disk name),(ID number)(return) to format a disk.
  :FL R0:(new name)=(old name)(return) to rename a file. Do not use any of
  the :FL commands if you already have a file open, or you will corrupt
  the disk. Refer to your Drive Manual for other DOS commands.
 
  :FRack #. Where # is a number between 2 and 255 and is the period of
  time in seconds between sending a packet signal, and if it is not
  acknowledged, will send the same packet again. Default 6.
 
  :FRQ ON or OFF. This sets the Mains frequency in Cycles (Hz). OFF is for
  50 Hz. ON is for 60 Hz. Default OFF.
 
  :Getp #. Where # is a parameter file number between 1 and 9 that has
  previously been saved to disk via the :S facility. (See the :SAvep
  Cmd.) For example :G 5 (return) will get the PRMTXA 5 file from disk and
  transfer it to the MB-XA 64 programme replacing the existing parameter
  file. The programme will always Fire Up with PRMTXA 0, so default is 0.
 
  Help is a cmd used by another station connected to your station. ie, if
  the other station sends H, a Help file (O File) is taken from disk and
  transmitted back to the connected station.
 
  Info is used by a connected station who seeks Information about your
  station. This information should be written to disk as the M File using
  the :WF cmd or the word processor.
 
  :IOport ON or OFF. When ON, will allow for SERIAL DATA to be taken from
  the USER PORT for feeding to an external Centronics Interface for the
  connection of any printer that will accept SERIAL DATA. A Parallel
  printer will not work direct from the USER PORT.
 
  Jheard is used by a connected station who wants to see the stations that
  your station can hear. Format J(return). To see your own Jheard stations
  simply press F5.
 
  :Kill #. Where # is a msg number or numbers separated by a comma for
  killing unwanted msgs. Example: You have 20 msgs on your U file (Msg
  file) and you want to erase 5 of them, say msg numbers 1 to 5. You would
  type :K 1,2,3,4,5(return). If you watch the screen between the status
  lines you will see a sequence of commands that the :K cmd sets in
  motion, NOTE: You must only kill those msgs sent to you. DO NOT KILL
  MSGS THAT YOU HAVE WRITTEN USING THE :SP CMD as these are allocated a
  BID NUMBER, and if you kill them you will prevent the Auto Forwarding
  from working correctly. Those msgs which have been forwarded will be
  killed automatically just after midnight every night. The highest msg
  number that can be used is 255. Numbers above this will Lock Up the Auto
  Forwarding routine. YOU HAVE BEEN WARNED!
 
  KMine is used by a connected statiol to erase a personal msg that you
  have left on your msg list. Format is KM(return). While your station is
  carrying out the KM cmd, the connected station will RX the msg MSGS FOR:
  (callsign) Being Killed. This cmd is also used in direct mode for
  clearing the whole msg file. Simply type :KM(return). All msgs will be
  erased and the U file reset to 0. This cmd will only operate when not
  connected.
 
  IMPORTANT NOTE: The Maximum number of files on a floppy disk must not
  exceed 140. If this fieure is reached, and even if there is still many
  empty blocks available, the disk will not accept any more files.
 
  :SP is used on the XA version in direct mode for writing messages
  to the U file for Auto Forwarding or for attaching to your MAIL FOR
  Beacon. You must not be connected to another station when using this
  cmd. Type :SP (callsign):(subject)(return) for writing a msg to be read
  from your mail box. (A Mail For Beacon will be transmitted every 30
  minutes to inform the station that he/she has mail on your system.)
  To write a msg for auto forwarding to another station via the BBS
  network, type :SP (callsign)@(BBS callsign):(subject)(return).
  You will notice that the TX screen will change and the cursor will drop
  into the RX screen when using the :SP. Write the msg and end with a
  CONTROL Z to save it to disk.
  To send a bulletin to a BBS type  :SB ALL @ GBR:(subject)(return).
  To place a bulletin on your PBBS type :SB ALL:(subject)(return).
  Make sure to type a colon (:) before entering the subject or it wont
  work properly.
 
  You can also Auto forward to any other MB-XA station provided you can
  connect to them either direct or via a Node Path. For example: My :PATH
  is G8EIA, BRAM,2 G4FIS-2,1 G7AMW-2. The -2 is the port 2 Mail Box of
  G7AMW, who is another MB-XA user.
  My :MFWD parameter is set at GB7NEM, *G7AMW-2. I enter sp g7amw @
  g7amw:(subject)(return). The -2 is appended to the callsign
  automatically so does not need to be entered. After entering the msg and
  ending with a CONTROL Z, the msg goes into the Auto Forwarding list and
  will be forwarded via the Node PATH to the personal Mail Box of G7AMW.
  If the msg fails to get through the first time it will be transmitted
  every 30 minutes until it does get there.
 
  :LCase ON or OFF. When set to ON will ensure that all characters typed
  are in lower case. In this mode, pressing SHIFT and a letter will give
  upper case. (Capital Letters.) When OFF, all characters will be in upper
  case. Defawlt ON.
 
  LM (List Mine). This is used by a connected station to see if there are
  any msgs or bulletins on your PBBS for them.
 
  :LINkt #. (Link Time). Where # is a number between 6 and 255 and
  represents a time period multiplied by 10 seconds. If connected to a
  remote station and nothing is heard for the time given in #, then the
  programme will check to see if the link still exists. If nothing is
  heard, a number of retries, as set in the cmd :RETry (see further on)
  will determine if the link is still open before diconnecting. Default
  30.
 
  L is for use by a connected station to List your msg file. If no msgs are
  found for them they will RX NO MSGS FOUND FOR: (callsign) followed by
  your command line. ie: G6WWW:- C,B,H etc. Use in direct mode by typing
  :L(return) to view your own msg list.
 
  :MAxframe #. Where # is a number between 1 and 7 and represents the
  number of packets for each Frame to be transmitted. On busy frequencies
  or if transferring programme files, set to"1. default 2.
 
  :MFIlter (characters). This parameter is used to set which signs are to
  be displayed on the main 80 column monitor scor specific
  stations, then put their callsigns here. ie :MFRom G0000,G0001,G0002
  (return) will only show to the main monitor screen the packets
  transmitted by these three stations. Default ALL.
 
  :MONitor (control letters or OFF). The letters are tokens which control
  what is to be shown on the monitor screen. ie: M=Monitor ON or OFF.
  C=Monitor ON even when connected. T=Your packets shown on monitor.
  A=Callsign of sender to be shown. D=Digipeater chain to be shown.
  E=Callsign of receiver to be shown. K&S=Status of packet cmd to be
  showl. ie: RR. SABM. IACK. INFO etc. (See Packet Codes for details.)
  L=Linefeed after each packet. The default settings are: MT ADEK UISQ.
  NOTE: It is best to turn the monitor OFF when using the :WF facility.
  This is to prevent any unwanted monitored text from mixing with the text
  you are writing. Format is :MON OFF(return). What this does is to delete
  the M from the control letters. Type :MON(return) and you will see that
  all the control letters are still there bar the M. Typing :MON
  ON(returl) will reinstate the M and so turn the monitor back ON.
 
  :View. Use this cmd to View (read) any sequential file from your disk.
  (Including mail.). To read a file type :V (filename)(return). Pressing
  the Space bar will halt the file, press again to continue reading. To
  abort from a lengthy file press the Space bar followed by RUN/STOP key.
GET XA-MANUA.6
 
    6 OF MB-XA INSTRUCTIONS.     Copyright (C) JSM GROUP 1992.
    """"""""""""""""""""""""""""""""""""""""""""""""""""""""""
 
  :Morse ON or OFF. If ON, will transmit a CW ID every 30 minutes. (Cursor
  will freeze while CW is being transmitted.) The ID is taken from the
  callsign in port 1. Default ON. (UK Licence Conditions.)
  NOTE: Morse works independent of the clock.
 
  :MPort #. Where # is any 1 of your 3 ports. For example: type :MP
  2(return) and port 2 will become your main monitor screen. Default 1.
  (Access to each port is by pressing CONTROL and the port number.)
 
  :MYcall (callsign). Where callsign is your callsign designated to each
  port. Example: Press CTRL and 2 to enter port 2. Type :MY FRED (return)
  and port 2 will now show FRED. The callsign in port 1 must only be your
  normal callsign without any SSID. (Secondary Station Identity).
 
  NODE CODES reads the Node Codes when 2 Nodes are connected and the
  information is displayed to monitor as:
 
    CONN. Connect request.
 
    CACK. Connect Acknowledged.
 
    INFO. Information follows.
 
    IACK. Information Acknowledged.
 
    DISC. Disconnect request.
 
    DACK. Disconnect Acknowledged.
 
  N (Nodes Heard). Used by a connected station to see what Nodes your
  station can hear direct. Example of use: If the station wants to connect
  to a station that is out of his range, then he/she can read the Nodes
  Heard list from stations that you can connect to until he/she finds a
  station that shows the callsign of a station that is within reach of the
  station that he/she wants to connect to. If the station has a Node port
  they would type C (callsign the station they want)(return).
  Alternatively, they could type :C (callsign of the station they want)
  via (callsign of the station that can reach him/her )(return).
  NOTE: Your Node list is compiled by you as the N File. Use the :WF cmd
  or the word processor to write this list.
  You should only enter those Nodes that your station can connect to
 "either direct or via another Node.
 
  PACKET CODES SHOWN ON MONITOR.
  {C}. Connect cmd. {D}. Disconnect cmd. FRMR. Frame reject. UA.
  Un-numbered acknowledgement. RR. Receive Ready. RNR. Receive Not Ready.
  RJ. reject packet. (Probably Corrupt.) UI. Un-numbered Info. I#.
  Information packet. Where # is the packet number.
 
  :PAClen #. Where # is a number from 10 to 255, and is the number of
  characters (and spaces) that will be sent as a packet. ie: If PAClen is
  set to 70, then after 70 characvers have been typed they will be
  transmitted as a packet. Should be set to about 60 for slow or difficult
  paths. Up to 150 for normal use. 255 for very quiet frequencies. Default
  100.
 
  :PASsall ON or OFF. When ON will allow corrupted packets to be displayed
  on screen. Default is OFF.
 
  :Savep #. Where # is a number from 1 to 9. This command allows you to
  save up to 9 sets of different parameters to disk. The default value of
  0 is automatically loaded when the programme is fired up. Exaople of
  use: you have cjanged some of the parameters and want to store them on
  disk for future use. Type :SA 1 (return) and they will be saved to disk
  as PRMTXA 1. To recall them back into the programme type :G 1 (return)
  and they will be called from disk to replace the parameter file already
  in memory. You may have to reset the Clock and date each time the :Getp
  cmd is used.
 
  :PATH (OFF or known pathway of Nodes). eg :PATH MI21, G8GPO-2, RHB21,
  G1UWS-1, G9ABC: To connect to G9ABC you skmply type :C G9ABC (retupn)
  and the system will automatically follow the path and eventually connect
  to G9ABC. Each callsign must be followed by a comma except for the last
  station in the Path which must end with a : (colon). Any of the stations
  in the Path can be accessed individually. ie :C RHB21 would stop the
  Path when that station was connected to. The maximum length of the path
  is 80 columns including the cmd and spaces. (1 screen line). This
  parameter will only work with nodes that give little or no connect text,
  such as THENET, KA, Digiprom etc. The reason for this is faster access
  times with less traffic congestion of the air ways. If the Path includes
  a Node which returns a lengthy connect text, digiprom will disconnect
  and return the msg FAILURE WITH (callsign). To connect to a Node or
  callsign in the Path without invoking the routine, simply type :CON
  (callsign)(return) and this will bypass the :C routine.
 
  :Printer ON or OFF. Quite simply turns the printer On or OFF. When set
  to ON, the printer will be initialised to the parameters set in PRTRSET.
  The printer itself must be turned ON before setting this cmd to ON,
  otherwise it may cause the programme to hang. If it does, then reset the
  computer. default OFF.
 
  :PRTRset # # (A B C). Where # # is the secondary address for the printer
  (if required) and A B C can be between 0 ald 255. Non Commodore printers
  will have these extra addresses in their respective manuals. Commodore
  printers such as the 801, 802, 803 and the 1101 should print text
  exactly as received by setting :PRTRset to 7 0. Default 7 0. (See also
  the IOport cmd). NOTE: Digiprom was written specifically for Commodore
  printers, and while some other types of printers may work satisfactory,
  some will not work at all.
 
  :RCMD displays all the remote parameters with their default settings to
  the top half of the screen. To see them all in one go type :DIV 22
  (return) followed by :RCMD (return). The number 5 indicates that the
  parameter is OFF. ie: no one has remote access to that particular
  parameter. The number 0 (zero) means ON. To change a papameter for
  remote use by other stations type :RCMD (parameter) 0 (return) for ON,
  or 5 for OFF. Default LEAVE AS IS.
 
  Read (file name). This is used when connected to another station for
  reading files from their disk, such as a msg from another Digiprom
  station, or a bulletin from a BBS. Format R # (return) where # is the
  number of the msg/bulletin. This cmd is also used for taking a file from
  your disk and transmitting it to another station. For example: You have
  written a msg/bulletin via the :SP function and you want to send it
  manually to a connected station. All you have to do is type :R (msg
  number)(return) and the file will be transferred to the other
  station. Dont forget to close the other stations disk with a CTRL Z or
  /EX at the end of the file. Default is OFF.
 
  :REMote (ON or OFF). When ON, allows a connected station to send remote
  commands, but only those which are set to 0 in the :RCMD parameter.
  Default ON.
 
  The following remote commands must always be set to ON. (0). LIST. LAST.
  LM (List Mine). KM (Kill Mine). Jheard. NODES. USERS. BYE. DISC. INFO.
  READ. SP. SP.MSG. SP.MSG#. /EX. WP. WS. CBELL, HELP. ?. CONNECT. WRPG.
  RPRG. SB.MSG#.
 
  :RESptime #. Where # can be any number from 1 to 50 and is the time in
  1/10th of a second which waits for an I frame from the connected
  station. Default 10. (1 second.)
 
  :RETry #. This sets the number of retries before returning to monitor or
  disconnect when no response is detected from either the connected
  station, or a station you are trying to connect to. The default is 20.
  (Actual retries is approximately one third of the chosen number.)
 
  :RNot (callsign's or NONE. The callsign/s following :RNot will not have
  use of the remote facilities from your station. ie: They wont be able to
  use L, LM, R etc etc.
 
  :RECon will attempt a reconnection to the last station you were
  connected to. There is no need to type in a callsign.
 
  :RPrg (programme name). This command allows you to read programme files
  from disk and send them to another station. Used without the colon (:)
  when connected to read a programme file from the other statimns disk.
  Dont forget the CTRL Z or /EX when the file has been transferred, either
  way. Default OFF.
 RMine (Read Mine). Used by you for reading a personal message from your
  local BBS. Dont forget KM (Kill Mine) to erase it after you have read
  it.  Not used in Digiprom MB-XA.
 
  SP (Send Personal). Used when connected for sending a personal msg to
  another Digiprom station or to your local BBS. When used with Digiprom
  MB-XA the format is: SP (callsign)(return). Any BBS use requires SP
  (callsign) @ (BBS destination callsign.)
 
  :ST #N. Where # is a letter and N is a number and refers to the text
  stored in the Send Text memory. To view the send text, type :DIV
  22(return), then type :SL (return). Approximately half of the ST
  memories will be shown on screen. To see the remaining memories simply
  press return at the line with SLIST CONT on it.
  NOTE: ALL of the text stored is used by the operating system and should
  not be altered.
  Remember vo type :DIV 8(return) to get back to the normal screen.
 
  :TEST ON or OFF. If ON, the control tokens are shown in reverse video
  but functions are ignored. Default OFF.
 
  :SList. Shows the ST Memories as above.
 
  :TRAn #. Where # is any text stored in any memory location. For example,
  :TRAn BT(return) would transmit your beacon text.
 
  :TXDelay #. Where # is a number between 5 and 40 and is multiplied by 10
  to give a time period in Msecs which is the delay between PTT and actual
  transmisqion of the packet. eg: If TXDelay was set at 25, then
  multiplied by 10 would give 250 Msecs. (.25 of a second.) Default is 30.
 
  :UNProto #. Where # can be CQ, ID etc. Similar to Baddress. Used for
  calling CQ by typing without the Cmd colon (:) when not connected. All
  the text that you type will be appended to your callqign and transmitted
  when return is pressed. Example, :UNProto CQ(return). Delete the colon
  (:) from the next line and type DOES ANYONE WANT A CHAT.(return). A
  beacon will be transmitted as: Your callsign>CQ>UI DOES ANYONE WANT A
  CHAT. Default ID.
 
  Users. Used by a connected station to see a list of your ports and their
  status. Used when not connected with a colon(:) ie :Users to view your
  own ports.
 
  :View (file name). Use this command to View (read) a sequential file
  from disk without transmission of the text. To stop the text from
  scrolling off the screen press the Space bar once. Press again to
  continue Viewing. If it is a long file, such as this one, and you have
  read the part which was of interest to you, then press the Space bar
  once to stop scrolling then press the RUN/STOP key to abort the :View
  command. Files can be Viewed from any one of the 4 ports, but if you are
  viewing on the same port as the monitor incoming text will be mixed with
  the file you are reading. Viewing is best done with the radio OFF. You
  can of course turn the monitor OFF with :MON OFF(return). This simply
  deletes the M from the characters. typing :MON ON(return) will reinstate
  the M and so switch the monitor back ON. :View can also be used in
  direct mode for appending a file or msg to a msg or bulletin that you
  are writing with the :SP cmd. eg: when you have finished the
  msg/bulletin dont press CONTROL Z, instead, type :V (filename) (return).
  The file must be on the same disk as the U file. When the cursor comes
  back, delete the colon (:) and type CONTROL Z (return). You wont see the
  file being appended, but if you type :L(return and then :V *last msg
  number)(return) you will see that the file has indeed been placed into
  the msg/bulletin. Note: Adding a file to a msg using the :V cmd will
  take several minutes.
 
  :CLS (return) will quite simply clear the RX screen.
 
  :WSfile (file name). This is a direct command and is used for
  downloading messages or bulletins from a BBS or any other station direct
  to your disk. WSfile meaning nothing more than Write Sequential File.
  Example: There is a bulletin on your local BBS that you would like to
  save to disk for future reference. Connect to the BBS and then type :WS
  (bulletin name)(return) to open a file on your disk, then type (without
  the colon :) R (bulletin number)(return) and the file will be saved to
  disk. Type :WS OFF(return) to close the disk file, and then disconnect
  from the BBS. You can read the bulletin as many times as you like by use
  of the :View command. Is also used when connected to another station for
  sending a file to that stations disk. Make sure to end this use of WS
  with WS OFF (return) to close the other stations disk file. Note: A file
  sent with WS will not be shown on the receiving stations msg list.
  Default OFF.
 
  :XM ON or OFF. If OFF then no transmission will take place. Use this
  command for self connects to check your equipment, or for practice or
  experimentation.
 
  ? is a command used by a connected station to get call the O file (Help
  File) from disk.
 
  In response to the many requests asking for clarification of the :ATEXT
  Parameter. :ATEXT is the alternative connect text that a station will RX
  when connecting to your station. eg: type :A(return) and you will see
  the callsign of your local BBS with a colon (:) and a letter appended,
  (usually C.) The letter denotes which section of the Send List will be
  transmitted when your BBS connects to you. Any other callsigns written
  here should only be Digiprom MB-XA  users with a :D at the end of each
  callsign. This will ensure that they RX the correct :AText fop Auto
  forwarding msg to you. A sample list is in place for you to alter.
  You can have up to 5 callsigns in the Atext provided that each one is
  separated by a comma. eg: GB7NEM:C, G7AMW:D, G1SFK:D, G6WWW:D etc.
 
  Digiprom MB-XA 64 will accept any 4 to 8 digit callsign beginning with a
  numeral.
 
  The command V has been added to allow a connected station to see what
  version of Digiprom you are using. And also, KA Nodes are now accepted
  by the Digiprom Node.
 
  Certain types of Nodes, due to their "Digi" style performance will not
  be accepted by the MB-XA 64 Node, and a disconnect will occur if you
  should try to access one. The Nodes accepted by MB-XA 64 include THENET,
  THE NODE. KA. Digicom. Digiprom MB-XA etc.
 
  You may find several colons (:) tagged onto the end of your PATH
  entries. Don't worry, they do not need deleting, even if they continue
  to the end of the line. They are the result of a "Fail Safe" routine
  which prevents a PATH being transmitted when it contains no end
  callsign.
 
  IMPORTANT. If you have msgs on file waiting to be Auto Forwarded YOU
  CANNOT ALTER THE PATH.
 
  Do remember that the use of a Node (or BBS) is a privilege, not a god
  given right. Abuse that privilege and you will surely lose it.

  FILES NEEDED ON DISK FOR PBBS/BBS OPERATION.
 
  PRMTXA #. This is the message management file.
  U This is the actual message storage file.
  M1. M1. M3 are the programme files.
  PRMTXA 0 is your Parameter file.
  All of these files are created automatically from the MAIN MB-XA DISK to
  a Work Disk.
 
  PBBS MAINTENANCE. Do make frequent use of the :FL V0 command. This will
  ensure that all files on your disk will be kept separate and in good
  order. Only used when not connected. Always use this command after
  scratching files or erasing them with the :K or :KM commands.
 
  The Digiprom series of packet software is Copyright to the JSM GROUP.
  However, licence is granted to any licensed radio amateur to copy and
  use the software, and to make copies for the exclusive use of other
  licensed radio amateurs provided no charge is made. Copying by any non
  licensed amateur, commercial enterprise, or any user group other than
  D.P.U.G. is strictly forbidden without the written permission of the JSM
  GROUP.
 
  No computer programme is completely bug free, so if you think you may
  have found one in MB-XA 64, then please inform us at the address on the
  disk Sign On Screen so that we can put it right. But do make certain
  that it is not an error on your part, so do read these instructions
  thoroughly and only use the commands listed.
 
  Digiprom MB-XA 64 can be used by your local BBS to auto forward personal
  mail to your disk drive. Ask your local BBS sysop if he/she is prepared
  to put you on his/her forwarding list.
 
  NOTE: All of the Parameters and Commands contained in these pages are
  applicable to an 80 column screen only.
 
  Do remember that msgs or bulletins you are downloading from another
  station will rapidly scroll up and off the screen from where it cannot
  be recovered, so do use the :WS cmd to save them to disk.
 
  If you should have any problems when using MB-XA 64 then please feel
  free to contact us at our Billingham P.O. Box which can be found on all
  versions of Digiprom.
 
  These parameter and command files were compiled by the JSM GROUP on the
  JSM 128 Word Processor, and although every effort has been made to
  ensure these instructions are correct, no liability is accepted for any
  errors, whether typoghaphical or otherwise.
 
  Digiprom MB-XA 64 is available free of any charge from any D.P.U.G.
  Copier. Howeter, you must supply a clean formatted 5.25 floppy disk and
  a prepaid return disk mailer. Or alternatively, enough cash (UK Sterling
  or US Dollars) to cover cost of same. A minimum of |2 is suggested for
  UK and EEC countries, and $10 for all other countries. For your nearest
  Digiprom copier contact:
 
    PAUL TIMMINS. G0NDV
    60. BRAMWELL STREET
    NETHERTHORPE
    SHEFFIELD
    SOUTH YORKSHIRE
    UK. S3 7PA
 
  Or Contact by Packet is G0NDV @ GB7BSX
 
  The 128 version of MB-XA is designed for true 80 column display via an
  RGB monitor which must be connected to the D shape RGB outlet on the
  rear of the computer. However, Composite monitors can be used if they
  are wired correctly to a 9 pin D plug. ie: Solder the Video wire from
  the monitor to pin 7 on the plug, and solder the Ground wire to pin 1 on
  the plug. This completes the video connection.
 
  If your Composite Monitor is equiped for sound then you will also need
  an 8 pin DIN plug wired in this manner. Solder the Audio uire from the
  monitor to pin 3 on the 8 pin plug, and that's it. No Ground is
  required. Push fit this plug into the Video socket of the 128 and you
  can now use your Composite monitor for 80 column plus sound.
 
  Follow the On Screen Instructions from the MAIN DISK to create a Work
  Disk.
 
  Do make a backup Copy of the whole programme disk by using any disk copy
  programme. NOTE: Programme files cannot be copied separately.
 
  Digiprom MB-XA 64 will work in 64 mode on both the C128 and the 128D
  series with either a 1541 MK1 or MK11, or a 1570/1571 disk drive. Note:
  Loading times are considerably slower when a 1541 drive is being used.
 
  :TPUK ON or OFF. When ON will stop your station from receiving Third
  Party Mail. (UK Licence Conditions.) When ON will allow Third Party msgs
  to be written and read from your PBBS.
 
  :MFLT (return) will display to screen the numbers of any msgs waiting to
  be Auto Forwarded. If none are found and the SD box is lit (reverse
  video) then type :V (return) to reset SD. (Allowing for the Magic Minute
  system check.)
 
  :MFWD (local GB7 BBS callsign), *(callsign of other MB-XA user).
  This is the parameter for Auto Mail Forwarding to your local BBS and to
  any other MB-XA station that you can connect to either direct or via a
  list of Nodes as entered in your :PATH parameter.
  The first callsign must be that of your local GB7 BBS followed by a
  comma and a space. If you have not yet made a Work Disk from the MAIN
  DISK and followed the SETUP file, then do so NOW and read this XA Manual
  8 file from within the programme by typing :V XA MANUAL 8 (return).
  Press the Space Bar to pause and again to continue viewing.
 
  Having completed the SETUP file, type :MFWD (return). This will show to
  screen your Mail Forwarding station list. Your local BBS is shown at
  position 1 followed by a comma, a space and an asterisk and several Xs.
  These Xs represent the callsigns of any other MB-XA stations that you
  can connect to. When you get to know of other MB-XA users, simply type
  their callsigns over the Xs. Up to five callsigns can be entered.
  (Maximum 8 digit callsign including SSID.) But do remember that a space
  and a * must precede every callsign and that a comma must follow each