=============================================================================
 
     GGGGGG    BBBBBBB    777777777    BBBBBBB      BBBBBBB      SSSSSSS
    GGGGGGGG   BBBB BBBB  777  7777    BBB  BBBB    BBB  BBBB   SSSSSS
   GGG   GGG   BB     BB      777      BB     BB    BB     BB   SSSS
   GG          BBB   BBB      777      BBB   BBB    BBB   BBB   SSS
   GG          BBBBBBBB    77777777    BBBBBBBB     BBBBBBBB    SSSSSSS
   GGG   GGGG  BBB   BBB     777       BBB   BBB    BBB   BBB       SSS
   GGGG   GGG  BB     BB     777       BB     BB    BB     BB      SSSS
    GGGG GGG   BBBB BBBB     777       BBBB BBBB    BBBB BBBB     SSSSS
     GGGGGG    BBBBBBBB      777       BBBBBBBB     BBBBBBBB   SSSSSSS
    
=============================================================================






                              -------------------
                                USERS HAND-BOOK
                              -------------------



                                Updated 01-Jan-1994
  


                                   F6FBB v5.15b



                       PACKET RADIO BBS & SERVER SOFTWARE
                       ----------------------------------




                  MULTI-PORT    MULTI-CONNECT    MULTI-LINGUAL












                          Documentation prepared by:

  

                              
                             Andy Witts - G1DIL  
                          SysOp @ GB7BBS.#28.GBR.EU
                                




Overview
--------

This documentation is written primarily for use by the local users 
of my Mailbox and Server system GB7BBS, in the hope that they can 
further enjoy the ever expanding facilities available from the FBB 
package.  I have made this text available to other SysOps such that
it may be distributed, to other users across the Packet fraternity 
to also help them get the most from their local mailbox systems. 

As a result of the extreme flexibility of the FBB Mailbox package, 
and the wide range of additional Servers and Utilities which can be
integrated with it, there may be some external facilities detailed 
here which may not be available at systems other than GB7BBS. 
Conversely, other systems will probably have other facilities 
available which are not documented here. I hope that all of the 
integral FBB facilities are, however, covered.

Some of the text is taken from associated documentation and some is
original. It is therefore not copyrite and FBB SysOps are free to 
edit and re-distribute the text to their users as they so desire 
provided that acknowledgement to this document is clearly recorded.

Acknowledgements: 

To Jean-Paul Roubelat, F6FBB for a very fine Mailbox program package,
long may he continue with it's development! 

To Per, LA6CU for his continued work with the English translation of
the FBB SysOps manual.

To all the authors of complimentary software for use with FBB.

To anyone from whom I have taken and adapted parts of their 
documentation.



BBS/MAILBOX COMMAND LIST:
-------------------------

This is a brief listing of the user commands available:-

? : HELP        - Sends the help file header.
A : Abort       - Abort listing or ascii file transfer.
B : Bye         - Log off (disconnect).
C : Conference  - Access to the round-table conference.
D : DOS         - Access to FBB-DOS, or to download a file.
F : Facilities  - Access to Server mode.
FP: Find Path   - Search disk for a particular filename.
G : Gateway     - Cross-Band Gateway
I : Info        - Information about the system hardware.

White Pages commands:-

I  callsign:    - Show the White Pages entry for that user.
I@ destination  - List all users registered at a particular Mailbox.
ID              - Shows the number of live WP records on-file.
IH callsign:    - Show full heirarchicaÿ address.
IZ Postal Area: - List users registered in a particular postal area.

J : Jheard      - List of the last 20 connected stations.
K : Kill        - Kill messages.
L : List        - List messages.
M : Make        - Copy a message to a file.
N : Name        - Input/ammend your first name.
NH: HomeBBS     - Input/ammend your HomeBBS.
NL: Location    - Input/ammend your Town or City name.
NQ: QRA         - Input/ammend your QRA locator.
NZ: Postal area - Input/ammend your Postal Area.
O : Options     - Select/change user options.
PS: Servers     - Show which servers are available.
PG: Program     - Show DOS-programs available to Users.
R : Read        - Read messages.
S : Send        - Send messages.
T : Talk        - Page the SysOp.
U : Upload      - Upload a file to the mailbox.
V : Verbose     - Verbose read of messages (like R, but with full headers).
W : What        - Which files are available.
X : Expert      - Change between Normal and Expert.
Y : Yapp        - Transfer binary files with Yapp transfer protocol.
Z : Delete      - Delete a file.
> : T.e.x.t     - To send a text to another station connected to the BBS.
= : Connect     - To connect another station connected to the BBS.
! : BBS Status  - Display system status.
# : Mail for    - Shows list of callsigns with unread mail waiting
* : Wildcard    - Use to speed commands/searches. (@,?,#,=,* are all
                  acceptable see section on wildcards elsewhere for a
                  more detailed description of uses.)              


BBS/MAILBOX COMMANDS:
---------------------


Help is available at all times when connected to GB7BBS just type 
"?x" where "x" is the command letter or command name you are not sure 
of. Example:-

   For help on listing mail type:  "? L <return>"
   For help on using the REQDIR server type "? REQDIR <return>"

?   

The "?" alone sends the help file header.
The "?" with a qualifying letter gives a help file which is specific

to that letter. For example "?R" sends the help file for the command

"R"  which relates to Reading Mail -

!

This shows who is connected, and current Mailbox status.

# 

This shows a list of callsigns who have unread mail.
     
>

If you want to send a message to another user of the BBS who is
connected at the same time then precede your text with ">" and the
target callsign. The BBS will then advise that your 'break' has been
delivered. Example: If you are using the mailbox and after giving 
the "!" command find that OM G9AAA is also connected you could type

the following at the system prompt:-

GB7BBS : MAILBOX prompt >
USER   : > G9AAA Hi Fred call you on 3.650 Mhz at 20.00"

Note: This cannot be longer than one line (80 Characters).

= 

For background read the above relating to the > command. Should you
wish to establish a connect with another user of the mailbox on your
own, or any other port, simply type:

GB7BBS : MAILBOX prompt >
USER   : = G9AAA

The two users will then be connected, and mailbox operations will 
cease. Once you have completed your connect, you exit back to 
Mailbox mode by typing ^Z (Control-Z).

A
-
Aborts the output from the mailbox at any time. However, don't 
forget that you are obliged to take what data is stored in the TNC 
buffer at the time you instruct the BBS to stop sending.

B 
-
Disconnects you from the mailbox. 

D 
-
Move from mailbox mode into FBB-DOS, and access to the users own 
files area. The FBB-DOS manager is very similar to MS-DOS and most 
commands, wildcards and hierarchical directories are allowed.

If the D command is followed by a filename then an ascii file 
download  will be invoked.

F 
-
Toggles between BBS and SERVER (facilities) modes.

FP
--
Find Path to any file in the GB7BBS file area.

GB7BBS : Mailbox Prompt >
USER   : FP FILENAME.EXT   
GB7BBS : C:\DIRECTORY\FILENAME.EXT

Wildcards are also acceptable, and are recommended.
All of the known directories will be searched, and a reply 
might look like this:

GB7BBS : Mailbox Prompt >
USER   : FP FILENAME.*
GB7BBS : C:\DIRECTORY\FILENAME.TXT
         C:\DIRECTORY\FILENAME.EXE
         C:\DIRECTORY\FILENAME.COM


I 
-
Shows specific information about the BBS, it's location, the type of
equipment in use and how to contact the SysOp.

J 
-
Lists the callsigns either heard by or connected to the mailbox.

- JK : Shows the last 20 connected callsigns
- JA : Connected callsigns on port A.
- JB : Connected callsigns on port B, etc...

- J1 : Callsigns heard on port A.
- J2 : Callsigns heard on port B, etc...

There are currently 6 active ports, labelled A to F.


K 
-
Kills messages sent either to or from your callsign. Only You or The
SysOp can Kill messages addressed to your callsign.

- K msg# : Deletes a specific message number.

- KM     : Deletes all the messages to you, tha? you have
           already read. Messages which you have not read will
           not be deleted.

L 
-
Lists the message headers.

- L      : Lists any new messages since you last used this command.

- LB     : Lists bulletins

- LC     : Here users can specify a mask to only have listed those 
           message headers which match the input. For example, entering
           "LC AMSAT" will result in only messages addressed to AMSAT
           being listed with the "L" command. Reset this command to

           the default using "LC *". Only one mask category can be 
           accepted at any one time.

- LC ?   : Lists all "TO" fields currently active and number of 
           messages.

- LC *   : Resets the LC register to "All Message Types"

- LD     : Lists by date. 
           LD < 930101 to list mail older than Jan 1st 1993 
           LD > 920101 to list mail younger than Jan 1st.

- LM     : Lists any messages addressed to your callsign.

- LN     : Lists any new messages to you not yet read.

- LL #   : Lists the last nn messages. Eg: LL 30 lists last 30 
           headers.

- LS xxx : Searches for a text string in all of the message headers.

           Wildcards are supported but are not necessary as the 
           complete subject string is searched. Note, tthat this is
           probably one of the most powerful and useful features which
           is available to uers.  

           For example if you wanted a list of every message which 
           contained the word "radio" anywhere in the title you 
           would simply type "LS RADIO" and you would receive a 
           listing like:

           .....  Date        Subject

           @GBR   21-Aug-91   Radio Rally to be held in Highley
           @GBR   22-Aug-91   Sky Radio - New DJ joins Astra team
           @EU    25-Aug-91   Where to contact Radio Society of G.B
           @GBR   28-Aug-91   Wanted: Magazine #67 Practical Radio
           @GBR   01-Sep-91   Sunshine Radio - Any listeners?


- LR       :  Like the "L" command but lists messages in reverse  
              order.

- L< Call  :  Lists messages originated from the callsign
- L> Call  :  Lists messages addressed to the callsign.

- L@ BBS   :  Lists the messages posted via a particular BBS.

- L Msg#-  :  Lists all messages above the specified number.

- L Msg#-# :  Lists all the messages headers between the two 
              numbers. 

The header list show sthe type and status of each message. The
inclusion of a 'D' in this list signifies that the body of the 
message is made up of partial or all, data.

Note to TPK/PTM/BAYSEL Users:

GB7BBS supports the BROADCAST of message headers on all user radio ports.
Those who wish to take advantage of this should contact The SysOp.


M 
-
Make a message into a file in the FBB-DOS files area. Use the syntax:


- M msg# path\filename  : Note, if no path statement is given the
                          message will be placed in the root 
                          directory of FBB-DOS.

- MA msg# path\filename : Append a message to an existing file.

- MV msg# path\filename : As above but the header/router information
                          will be included.


N 
-

These commands are used to collect information about You for  
Mailbox Registration, the World-Wide White Pages database, and 
for local calculations made by the FBB Satellite Server.

You will be required to complete the whole registration procedure 
before you can gain access to the Mailbox. If any of your 
corcumstances (particularly your HomeBBS) you should record these 
using the Nx command as soon as possible. 

- N  : Input/modify your first name
- NH : <nput/modify your HomeBBS entry for mail routing.
- NL : Input/modify your known location (usually your city/town).
- NP : Modifies your password. (Only for telephone modem access)
- NQ : Input/modify your QTH locator. 
       This information is necessary for correct satellite orbital 
       calculation from your own location.  If it is not entered 
       then the default of IO82TK will be used.
- NZ : Input/modify your Postal Area, it is not necessary to specify
       your full Post Code only the first section, like WV16.


NEW
---

When in FBB-DOS typing the command NEW will generate a listing of 
all of the new files which have been uploaded/created since the last
time you used the command. This list covers all directory areas 
which you are authorised access to.


O (Options)
-  -------

Display and/or ammend you; various recorded user options.

- OL   : Lists the languages currently available.
- OL # : Selects a language.
- OM   : Toggle on/off the display of your oustanding mail at log-on.

- ON # : Defines a message base number for abbreviated user input. 
         For  example, "ON 37" will define message # 37,000 as the 
         base message number, so the command "R 25" will read 
         message #37,025. 
         
         Your base message number is recorded for future sessions.
    
- OP   : Toggles paging mode on/off.
- OP # : Specifies number of lines sent in paging mode before the 
         "Send CR to Continue or A to Abort" prompt is sent at the 
         end of the page.

- OR   : Toggles between the ability to read only the users own mail
         and bulletins and the complete mail listing.


PG 
--
Sends a listing of the user programs available to be run by users.


PS
--
Sends a listing of remote Server facilities currently available.


R  
-
Reading messages.

- RM          : Reads current messages which are addressed to you.
- RN          : Reads all the new/unread messages addressed to you.
- R msg# msg# : Reads up to six messages in one block.


S 
-
Sending messages or bulletins.

You are recommended to read the WHITE PAGES section as an addendum 
to this section (Sending Messages) as this provides further 
information regarding the automatic addressing and delivery of 
messages.


PERSONAL MESSAGES
-----------------

- S callsign     : Will send a message or a bulletin. If the type is
                   not specified, it will assumed that it is private.

- SP callsign    : Sends a private message.

  Note: The Mailbox will automatically add the address of the target
  callsign to the message header, so as an example you might send:-

  GB7BBS : Mailbox Prompt >
  USER   : SP PE0MAR
  GB7BBS : Address added: @PI8VNW.#ZH2.NLD.EU
  GB7BBS : Send title (only) of this message

  If the address of the target callsign is unknown to the mailbox 
  (in other words it is not recorded in the White Pages database) 
  you will be prompted to cancel the message and input the address 
  manually. You must then usÿ the following syntax:-

  GB7BBS : Mailbox Prompt >
  USER   : SP PE0MAR
  GB7BBS : Address unknown: Type ENTER to abort and readdress manually
  USER   : CR/LF
  GB7BBS : Your message to PE0MAR has been cancelled
  GB7BBS : Mailbox Prompt >
  USER   : SP PE0MAR @ PI8VNW.#ZH2.NLD.EU
  GB7BBS : Send title (only) of this message


- SB ALL         : Type this to send a message which can be read by
                   ALL of the users at GB7BBS.

- SB ALL @GB7xx  : Type this to send a message which can be read by
                   ALL of the users at another specific Mailbox in UK

  Note: 
  The syntax "S CALL AT BBS" is accepted equally as "S CALL @ BBS"

BULLETINS
---------


- SB ALL @xxx    : Type this to send a message which can be read by
                   ALL of the users at all of the other Mailboxes in
                   a specific Country. You have to use the recognised
                   ISO international abbreviation for the target
                   Country. You will find a list of these codes at 
                   the end of this file.

  Here are some examples:-

- SB ALL @GBR    : Type this to send a message which can be read by
                   ALL of the users at all of the other Mailboxes in
                   the UK.

- SB ALL @DEU    : Type this to send a message which can be read by
                   ALL of the users at all of the Mailboxes in 
                   Germany.

- SB ALL @USA    : Type this to send a message which can be read by
                   ALL of the users at all of the other Mailboxes in
                   America.

  It is possible to send a message to all of the mailboxes in a 
  particular continent, by replacing the Country abbreviation above
  with the Continent abbreviation instead. This practice is not
  recommended as it generates huge volumes of traffic. For example,
  if you were to send a message addressed:-

- SB ALL @EU     : Then this would send a copy of your message to
                   every single mailbox in the continent of EUROPE
                   which as a Packet Radio domain includes not just
                   the EC countries, but Scandinavia, all of East
                   Europe (Poland, Romania, Hungary etc) and all of
                   Russia. 

- SR Msg#        : Reply to a message just read or killed, or to a 
                   message of a specific number. The header is then
                   created automatically and if no title accompanies
                   your SR command then the original title will be 
                   used preceded by Re: xxx
 
- SC Msg# CALL @ BBS 

                 : Send a copy of a message or bulletin to the 
                   specified callsign. Copy messages are always type
                   P (private). Any text entered after this command
                   and before the /EX will be included ahead of the
                   copied message.

- /ACK           : The addition of the characters /ACK in the first
                   column at the beginning of the message text will
                   ensure that a message acknowledging receipt at 
                   the distant FBB type mailbox is returned to you.


T 
-
Page the SysOp by ringing the bell. Should the SysOp be not 
available within one minute, you will be advised accordingly and 
automatically returned to the normal Mailbox Prompt.


U 
-
Uploads a text file from the user to the root directory of FBB-DOS,
unless qualified with a path statement. The U command can be typed 
in at the normal mailbox system prompt, it's not necessary to access
FBB-DOS.


V
-
Reads messages along with their routing audit trail. Use commands as
listed under "R" above but add the V suffix. Eg: VM or V 1234 


W 
-
Lists the files which are within the root directory of FBB-DOS. 
This command can be followed by a mask specifying search criteria or
a directory name; in the latter case, the directory content will be
listed.

X 
-
Toggles between "Normal" or "eXpert" status, which gives either a
short or long mailbox prompt.

Y 
-
Binary transfers must be done using YAPP protocol at both ends of 
the link (that is you must be running YAPP ÿrotocol in your computer)

- YD File   : Download a binary file from the BBS TO you.
- YU File   : Upload a binary file from you TO the BBS. 
              You cannotÿreplace or modify an existing file.
- YZ File   : Delete a file from the binary files area

Note: Binary files carry the 'usual' filename extensions of .EXE .COM
.ZIP .ARJ etc.  GB7BBS does not segregate Binary and ASCII files, 
they reside alongside each other in their special interest 
directories.

Z 

Deletes a file from the FBB-DOS files area.




WILDCARDS
---------

Throughout the Mailbox and Server all wildcards are accepted, these
both speed operation and add flexibility to searches. The list of acceptable
wildcards is as follows:

Examples:

     * -- Matches 0 or more characters of any type.
     @ -- Matches any alpha character (a..z, A..Z).
     ! -- Matches any digit (0..9).
     + -- Matches any alphanumeric character (A..z, A..Z, 0..9).
     ? -- Matches any single character.
     " -- Escape. The next character in the pattern must match the character
	  in the target exactly. Wild cards will not be interpreted.


  97*	   --  Will match anything starting with 97 such as 97068,
	       97123, 97ABC, and 97.
  97???    --  Will match anything that starts with 97 and is 5 characters
	       long.  97068 will match but 9706 will not.
  97!!!    --  Will match anything that starts with 97 and has 5 digits.
	       97068 will match but 97ABC will not.
  @!@@@    --  Will match a 5 character callsign such as G1DIL, F6FBB, etc.
  2E!@@@   --  Will match standard Novice callsigns.
  "!"*     --  Will match *!
  !*	   --  Will match anything that starts with a digit.


My MS-DOS reference guide says the following:-

> You can use wildcards to perform the same task for a group of files,
> you don't have to use the same command repeatedly for each filename
> in the Group. You can use wildcards to specify groups of files. A
> wildcard acts as a substitute for a name or extension.

In FBB you can use wildcards to work with text as well as files, so
this will help broaden or narrow your search patterns.
Use wildcards in callsigns, in message titles, in filenames, in fact
you can use them just about anywhere. If they are not accepted any
place you will be advised with an *** ERROR message.



WHITE PAGES DATABASE
--------------------

This facility is often referred to but rarely understood by many. 
This is a thumb-nail overview of what the facility can do for YOU 
the Mailbox user, it is by no means a definitive description of the
White Pages Server itself.

White Pages can be thought of as a big Phone Book for Packet Radio 
Operators. When you need to know where to find someone, you look 
them up in the book, or in this case you ask the computer to fish 
the information out of it's database.

As with anything to do with computers, the information you get out 
is only as good as the information you put in; and this is extremely
important as far as White Pages is concerned, so please read the 
next section carefully so that you understand what's going on under
the covers.

Your local Mailbox knows who you are and where you live, you've 
already told it this information when you registered. You have given
your Callsign, your Name, your Town, your Postal Area and your 
HomeBBS details using the N, NL, NQ, NZ and NH commands. All of this
information has been despatched to the Central White Pages Server in
Britain which in turn has sent a copy to every other mailbox in the
U.K, and to the other National Servers throughout the World, so in a
short space of time all the Mailboxes which have a White Pages 
facility will know about You.

You can easily check your own White Pages entry. Nextÿtime you log 
onto the Mailbox do the following:-

GB7BBS : Mailbox prompt >
USER   : I G3KNB             <===== Use your own callsign here

And you will be shown the database entry for that callsign. In this
instance it would look like:-

GB7BBS :
   5934: 930108 G3KNB  @ GB7MAX.#28.GBR.EU  Ken ST15 Stafford

This shows that G3KNB is record number 5934 in the database, and was
last seen on January 8th 1993. His HomeBBS is GB7MAX, and his name 
is Ken. He lives in Stafford, postal area ST15.

So, you can see that the information you give to the Mailbox when 
you answer the Nx questions is very important, and it travels right
across the world. So, if you find any of your information is 
recorded incorrectly you should put it right at the first 
opportunity. Lets say that in this example G3KNB's record is 
incorrect as it shows his ZipCode (Postal Area) at ST15 when in fact

it should be ST16, it can be changed when you are connected to the 
Mailbox as follows:-

GB7BBS : Mailbox prompt >
USER   : NZ 
GB7BBS : Please enter your Postal Area >
USER   : ST16 

Once you have done this your local Mailbox will start the chain 
reaction which will update all of the other Mailboxes around the 
world with this change. Obviously, the most important aspect of this
information is your HomeBBS, please check that it is recorded 
correctly, if not change it as soon as you can. If you change from 
using one Mailbox to another you should update your HomeBBS before 
moving.

So, now all of the people in all of the places have access to your 
information. What good is that ... ?

Well lets say you want to correspond with someone in Michigan, USA 
you could search the Postal Area section of your local White Pages 
database. Here's an example:-

Knowing that Michigan is predominantly in USA Postal Area 48nnn you
could enter:ÿ

GB7BBS : Mailbox Prompt >
USER   : IZ 48* 
GB7BBS :
    700: 921116 WB8ZPN @WB8ZPN.#SEMI.MI.USA.NA ? 48180 Taylor, Mi.
    900: 921116 WB8H   @WB8H.#SEMI.MI.USA.NA ? 48314 Sterling Hgts
    995: 921116 IW4CEA @IW4CEA.#RA.ITA.EURO ? 48100 Ravenna JN64CK
   3317: 921123 KA8UNZ @KA8UNZ.#SEMI.MI.USA.NA ? 48197 Ypsilanti
   3379: 921123 WA8PEJ @WA8PEJ.#SWMI.MI.USA.NA ? 48813 Charlotte
   7163: 930113 EB2DJB @EA2URV.EABI.ESP.EU Rafa 48080 Bilbao

GB7BBS : Mailbox Prompt >

Similarly closer to home you could check who is operational in the 
Wolverhampton area by sending:-

GB7BBS : Mailbox Prompt >
USER   : IZ WV* 
GB7BBS :
     20: 930117 G1DIL  @G1DIL.GB7BBS.#28.GBR.EU Andy WV16 Highley
     60: 921113 G4FIF  @GB7BBS.#28.GBR.EU Dave WV5 Dave Wombourne
    371: 921113 G6GUH  @GB7MAX.#28.GBR.EU Pete WV16 Pete Bridgnorth
    388: 921113 G7FEF  @GB7BBS.#28.GBR.EU Jim WV7 Albrighton
    933: 921116 G7ALE  @GB7MAX.#28.GBR.EU Peter WV7 Albrighton
   1038: 921208 G6CYI  @GB7BBS.#28.GBR.EU Neil WV16 Bridgnorth
   2692: 921121 G7BPD  @GB7MAX.#28.GBR.EU Rick WV7 ?
   2695: 921121 G3ENY  @GB7BBS.#28.GBR.EU Geoff WV16 Bridgnorth
   4593: 921202 G8GMA  @GB7BBS.#28.GBR.EU DAVE WV13 Willenhall
   5797: 921219 G0ISI  @GB7BBS.#28.GBR.EU John WV7 Albrighton
   8455: 930122 G8ZWU  @GB7MAX.#28.GBR.EU Kev WV10 Wolverhampton

GB7BBS : Mailbox prompt >

You can start to see the flexibility of the system, and the 
information that is readily available.

Now, this is all very interesting and provides a useful service when
you want to know how to find someone in a hurry, but the power of 
White Pages is in addressing mail more than in the above. Those of 
you who currently send mail overseas will know what a bind it is to
have to enter the full hierarchical address of the target station, 
get one full-stop in the wrong place and it's lost forever. Well, 
with WP on-the-scene those problems just disappeared... watch.

Currently if you want to send a message to VE4DBK in Canada you 
would have to enter it like this:-

GB7BBS : Mailbox prompt >
USER   : SP VE4DBK @ VE4KV.#WPG.MB.CAN.NOAM 
GB7BBS : Message Title ?
etc..

From now on you can send it like this:-

GB7BBS : Mailbox prompt >
USER   : SP VE4DBK 
GB7BBS : Address added: @VE4KV.#WPG.MB.CAN.NOAM
GB7BBS : Message Title ?
etc..

The Mailbox will check the known address for the target station and
add it to your outgoing message, automatically. Only if the target 
station is unknown will the BBS return and ask you to enter the 
address?manually.

So, here is a list of the search and retrieve commands in White 
Pages that are now available for you to use to interrogate the 
database:-

-  I  Callsign : Displays WP record for that callsign
-  I@ BBS      : Displays the users of a particular Mailbox.
-  IH Zone     : Displays users within a zone (#28, #CENCA, CYP etc.)
-  IZ Post Area: Displays users in a Postal Area.

Normal DOS wildcards are allowed to assist in your searches.

Additionally, if you find that you can't find the HomeBBS of another
OM, and it isn't on file at your own Mailbox at that time, you may 
send an enquiry to another WP equipped mailbox to check if the 
information is available. To do this send an ordinary message laid 
out as follows:-

GB7BBS : Mailbox prompt >
USER   : SP WP @ GB7xxx 
GB7BBS : Message Title ? >
USER   : Wp Query               <--- Any title will do, it's not used.
GB7BBS : Message text  >
USER   : G1DIL ?                <--- List the callsigns followed by a ?
USER   : F6FBB ?
USER   : ^Z

You will receive a reply listing the HomeBBS for each of the 
callsigns listed in the message.

As well as recording the responses you make to the Nx questions when
you register with your HomeBBS, the White Pages Server also looks at
all of the message headers passing through the Network to collect as
much information about users and their location as possible. So, 
it's important that once you've registered with a BBS you stick with
it. As soon as you send a message from another BBS the header 
information will be collected, the WP Servers will be advised that 
they "think" you have moved HomeBBS, and unless you reconfirm that 
you haven't moved within 1 month then your records will be 
permanently changed to show you at a different BBS. So, please 
choose your HomeBBs and stay with it. If you have to move 
temporarily then please use the registration commands to re-confirm
your 'real' HomeBBS when you get back, just using the N command to 
re-enter your name will be sufficient to trigger the update.



CONFERENCE MODE
---------------

C :  This command puts you into the multi-user Conference mode, and
     you will need to use a different style of commands shown below. 
     Note, that all commands sent in Conference mode must be preceded 
     with a full-stop (point/period) otherwise the BBS will interpret 
     the text only as conversation to be delivered to all other 
     conference users:-

     .W  :  Gives a list of Conference users

     .C {port} CALLSIGN  :  Make a connect to another user and bring
                            them into the Conference. The use of the port
                            number in the connect script is optional, if 
                            omitted then the default port number is the 
                            one on which you have called in.

     .D CALLSIGN  :  Disconnects the user from the Conference

     .H           :  Sends the Conference Help file.

     .Q           :  Quit/leave the Conference, and return to BBS



Cross-Band Gateway
------------------

Callers to the GB7BBS mailbox have the ability to make cross-band 
connections to other users/facilities, by calling out from GB7BBS one 
a radio port other than that which they are originally connected.

So, a user who connects on, for example, 144Mhz  can make onward
connections into the local Network on any of the other 4 fequencies 
or bands available at GB7BBS.

Callers who make their connect from the PSTN Network, can cross
connect and call out on any of the available radio ports, but 
radio callers do not have access to the telephone modem.

You can monitor any of the available ports with the M-command

Gateway-commands :

C : Connect.
D : Disconnect.
H : Help (this text).
J : List of the last 20 monitored stations.
K : Converse mode.
M : Monitor on/off.
P : Go directly from one port to another.  
    Type P1 to connect from your current port to PORT1.
Q : Quit and return to MAILBOX mode.

> or ESC to go back to Command mode.

Using the Gateway:-

Firstly you are allocated a free channel on your log-in port. If the link 
is not busy it will be assigned and it will assume your callsign. You are
automatically in COMMAND mode, and your input will be considered as a
command by the TNC interface. The mode will switch to CONVERSE as soon as
a valid connection is established. The K command also changes to converse 
mode.

So you establish a connect as follows:- "C callsign V digi1,digi2 <return>"

You can now communicate on the cross-band link as if you were connected
directly within your own operating band.

(All commands in gateway mode must be sent in Cmd:mode.  Enter Cmd:mode by
sending a > (or press ESC) and then press ENTER.)

At the end of your QSO type ESC to enter cCmd: mode and then "B <return>" 
to disconnect from the other station. Type "Q <return>" to return to 
MAILBOX mode. 



SERVER COMMAND SET:
------------------

The server commands are specific to the individual modules:-

    Main menu
    C : Connect statistics.
    D : Library.
    Q : QTH locator.
    N : User Database.
    T : Satellite orbital computation.

    F : Toggles between BBS and Server modes
    B : Quit and disconnects


CONNECT STATISTICS
------------------

    This module provides statistical information about the mailbox usage.
    Current options are:-

    G : Global statistics for all Server activities.
        - Number of active messages.
        - Number of connects.
        - Times of connects.
        - Peak traffic periods.
 
    H : Histogram of usage day by day (for one week).
        - H [Callsign] gives histogram for a particular user and
          wildcards are accepted for this feature: Example "H G3*"
    
    I : Lists the callsigns that have connected to the server.
        The list is given in alphanumeric order and wildcards accepted.
    
    J : Histogram of usage hour by hour (for one day).
        - J [Callsign] gives a histogram for a particular user and
          wildcards are accepted for this feature: Example "H GB7???"
    
    L : Lists all stations connected, on all ports and channels, during
        the log period. This is presented in reverse chronological order.
    
    O : Percentage activity of each Server module.


LIBRARY
-------

In this module you will find lots of information and/or documentation
which relates to Packet operation. Unlike the FBB-DOS file area this
module can be thought of as an archive of information, which users can
browse through like the books on the shelf of a library, and take out
and read that which is of interest. Files are obtained by typing a number
only so now knowledge of DOS or file download principles are required.

This area is mainly updated by the SysOp, however, users are most welcome
to also contribute any files or information which they feel is of benefit
to others, by using the NEWDOC server which is explained in the Remote
Server commands section later in this file.

Some operators who are inexperienced in either MS-DOS or general file
transfers, who feel intimidated by the FBB-DOS area, should find that
the Library has plenty to offer in terms of information and is very easy
to use.

Key "D" from the Server Menu to access the LIBRARY and then "L" to list
the available Topics. The system has topic areas (like filing cabinet 
drawers) and files (like folders within a drawer). So you first have to 
enter the TOPIC of your choice, and then list the available files. 

Key the number of your chosen topic, and then "L" to list the files,
when you see something which appeals merely type the number of the file 
which you wish to read and it will be sent to you, with paging if enabled.

If you want to look in another TPOIC area you have to type "R" to refresh
the menu, and then the number of the new TOPIC area. Once in the new
TOPIC area type "L" to list the available files and then enter the number
of the file of your choice.



USER DATABASE
-------------

In this module you will have access to the user database. Users have
the option to input information to this database regarding their callsign,
name, QTH, Phone number, operating conditions etc.

You may select to search for information regarding other users. Also
you can opt to input information of your own station to swell the database,
and giveaccess to others.

    N : Modify your name and address.
    R : Research information specific to a user.
    I : List those callsigns (only) which are held on file.



QRA LOCATOR
---------ÿ-

The QRA (Maidenhead) locator is made up of 2 letters, 2 figures, and
2 letters according to your stations geographical co-ordinates.

It's possible to convert the QRA locator into Longitude/Latitude or
vice-versa. Also you can calculate the distance and bearing (azimuth) 
between two locators or calculate the sum of all contacts for your contest 
Log-sheets.

    B : Quit and Disconnect.
    C : Sum up all distances between one QRA locator and several others.
    D : Distance and Azimuth calcÿlation between two QRA locators.
    F : Switches back to the Server main menu.
    L : Converts Longitude/Latitude into QRA Locator.
    Q : Converts QRA Locator into Longitude/Latitude.


SATELLITES
----------

This module allows users to gain access to accurate and up-to-the-minute
information about the status of the Amateur Satellites currently in
service. The facilities include:

    B : Quit and disconnects.
    C : Display a file detailing the characteristics of each satellite.
    F : Switches back to Server main menu.
    P : Display the keplerian elements set for a particular satellite.
    T : Satellite in-range calendar calculation for your QTH.


When selecting the in-range calendar option you will be asked to supply
the date and the time to be taken into account for the calculation. This
can be input as some time in the future/past using DD-MM-YY and HH:MM, 
or two CR's will start the program in real time.

The geographical position of the "observer" is the QRA Locator of the
connected user, provided that this has been input previously using the
NQ command otherwise, the default QRA locator of the mailbox will be used.

Depending on the satellites, the calculation step is variable, and one
line of orbit paraÿeters will be displayed per step.This line corresponds
to a minimum elevation of -5 degrees that means that the satellite is 5 
degrees below the horizon.


FBB-DOS
-------

This is a brief listing of the user commands available with FBB-DOS:-

? and HELP          -  This help file.
O                   -  Options (paging, base-number etc.)
DIR                 -  Show directory listing (better using LIST).
EDIT                -  Edit a file.
CD                  -  Change Directory.
MD and MKDIR        -  Make Directory.
COPY                -  Copy a file. (10Kb Maximum)
DEL                 -  Delete a file.
RD and RMDIR        -  Remove a Directory.
TYPE                -  Download an ASCII file with paging.
GET and PUT         -  Transfer an ASCII file to or from the BBS.
BGET and BPUT       -  Transfer a binary file in GP/SP/TurboPacket protocol
XGET and XPUT       -  Transfer a binary file with XMODEM (128byte) protocol
X1GET               -  Download a binary file with 1K-XMODEM-G protocol
YGET                -  Download a binary file with Yapp (Radio connects) or
                       YMODEM, YMODEM-G or G-YMODEM-BATCH on modem connects
ZGET                -  Download a binary file with ZMODEM protocol
LIST                -  Show directory listing WITH descriptive labels.
PRIV                -  Go to a private directory allocated by the SysOp.
VIEW                -  See contents of .ZIP .ARC and .LZH files.
NEW                 -  See all new files since last NEW command.
EXIT, F and QUIT    -  Return to BBS mode.
B                   -  Bye (disconnect).

For more detailed help with any one command, type "? [COMMAND]" from
the system prompt, or refer to text below:-

When you enter FBB-DOS, the system prompt shows that you are located
in the root directory of a normal DOS hierarchical disk filing structure.
If you are unfamiliar with this it can be explained quite simply, as 
follows:

The fixed (hard) disk in any personal computer stores a vast quantity
of data. Most common these days is a 100 Mega-Byte drive, onto which can
be put many thousands of different files. If you decided to look for a 
particular file on this disk, and it were not organised in some way, you 
would have to search through every single file, to find your target file. 
Very frustrating!

Think then of the disk being a large filing cabinet with a number of
different drawers, each with a label showing what is the subject of the 
folders inside each drawer. The drawers can be thought of as directories 
on the hard disk. So like the filing cabinet the drawers or directories 
have the general name of their contents. One drawer may contain all data 
concerning Radio, whilst the second drawer contains all of the information 
concerning Satellites.


The labels on the drawers of the filing cabinet can be thought of as
the names of separate directories on the hard disk.  As you would open
the "Radio" drawer to find the different files about the subject, so
you would "change directory" to "Radio" to look at all the files related
to that subject. The system is hierarchical so various sub-directories
can lead off the first (or ROOT) directory, so keeping everything in
their own category.

The filing cabinet is hierarchical. The cabinet itself is like the ROOT
directory, showing the drawer labels telling you what categories are
available. Then each drawer (directory) will have folders inside them
(sub-directories), and in each folder will be some papers (the actual
files). It looks like this:



                                     ROOT DIRECTORY
                                           |
                                           |
                          +----------------+------------------+
                          |                |                  |
                        RADIO            PACKET              HOME
                          |                |                  |
                     +----+----+      +----+----+        +----+----+
                     |         |      |    |    |        |         |
                    RTTY      SATS   YAPP  |  PAKET5   ACCOUNTS  GENERAL
                     |         |           |             |         |
                     |      SATFOOT       TPK         LOTUS123   ADDBOOK
                 +---+---+                               |
                 |       |                            MORTGAGE
               G3WHO  LOGBOOK



Once you have accessed FBB-DOS you will see that you will be in the
root directory of one or more of the hard disks installed at the mailbox.
(Up to eight physical/logical drives are supported)

You are free to move around and discover what files are available on
which disk. To do this you need three commands; the first enables you to 
switch from one disk to another; the second and third show what directories
(and/or) files are available to you.

Use the command LIST, to list the contents of your directory. It should
look something like this:

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\>

AMSAT          <DIR>     This directory contains Satellite information
COMPUTER       <DIR>     This directory contains files for Computer users
RIGMODS        <DIR>     ÿ00's of modifications for 100's of radios
BINARY         <DIR>     All files from here on are in binary format
USERDOC1.TXT   8556      User documentation (Part 1 of 2)
USERDOC2.TXT   9221      User documentation (Part 2 of 2)

Note that the prompt (c:\) tells you that you are in the root directory
of drive c: and the text tells the user that there are 4 directories
(these are marked <DIR>) from which to choose from; and that in this
current directory there are two files which are available for download.

There is a log kept of your downloads and this is compared to your
authorised limit. Once this limit is exceeded then you will have to
wait until the following day to request further downloads. The counter
is reset at each nightly housekeeping event.
 
You may move from one drive to nother by specifying the drive letter
as follows:

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\>

d:

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
d:\>
 
For the purposes of the following example all files will be assumed
to be held on drive c:
     
Should the user be searching for a file concerning any modifications
that are available for his FT-ONE then the obvious next choice is to 
look in the directory named RIGMODS. To do this the second of the most 
common commands is necessary - the CD or "change directory" command. 
It is used like this:-

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\>

CD RIGMODS
c:\RIGMODS>
LIST

ICOM          <DIR>     Directory of various modifications to ICOM rigs
TRIO          <DIR>     Directory of various modifications to TRIO rigs
YAESU         <DIR>     Directory of various modifications to YEASU rigs

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\RIGMODS>

Note how the system prompt now indicates the users different position
in the tree-like structure of the directories.

The next step is yet another directory change, as the search path is
narrowed to files which only concern rig modifications for Yaesu sets
and so the choice now is to enter the YAESU directory, which is done
like so:

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\RIGMODS>

CD RIGMODS\YAESU        <-- Note: You must include the backslash

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\RIGMODS\YAESU>

list

FT290MK1.MOD     3496     Various modifications for FT-290r Mk.1 
FT690MK2.MOD     4521     Various modifications for FT-690r Mk.2
FT736MOD.PSK    12457     Modify FT736r for use with PSK modem
FT736MOD.9K6     9985     Modify FT736r for use on packet at 9600
FTONE-CW.MOD    11876     FT-1 Special narrow CW filter modification

Here the user is presented with a listing of the files which are contained
in the directory (Note: that the prompt is again modified to show your
actual position in the directory structure). Now the file download can
commence:

As this is an ascii file there will be no need at this stage to use
the YAPP binary transfer protocol. What will take place now is a straight
text transfer which the user can file to disk, or print upon arrival:-

Establish the exact name of the file to be downloaded. In this case
it is:

                         FTONE-CW.MOD

It must match 100% with that shown in the directory listing. For example
in this instance a filename of:

                         FTONE_CW.MOD

would not be acceptable; neither would

                         FT0NE-CW.MOD

so please be very careful. The command to execute the text download
is: "GET filename":-

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded  21Kb]
[Authorised 100Kb]
c:\RIGMODS\YAESU>

get ftone-cw.mod

The Server will then send the file just as if you had read it as a message.
When complete you will again receive the FBB-DOS system prompt and you
can continue. If the session is complete you can disconnect in the normal
way, or you can return back through the directory structure either one at
a time using the "CD.." command, or directly to the root directory using 
the "CD \" command.

Having established how to move through the directories and download
some ascii files here is the full overview of FBB-DOS.

The syntax and format of the various FBB-DOS commands are almost identical
to those in MS-DOS (r). Several additional and specific commands have been
added, as shown below:

    PUT  :  Used for ASCII file transfers.
    GET  :  Used for ASCII file transfers.
    YPUT :  Used for binary transfers using YAPP protocol.
    YGET :  Used for binary transfers using YAPP protocol.
    EDIT :  Used to activate the ASCII files editor.

Any file created by a user "belongs" to this user and cannot be edited
or deleted by any other user, except the keyboard SysOp.

    DIR [mask] : Displays all the files contained in the directory or
                 those corresponding to the mask if specified. If the
                 mask matches a directory name, then the contents of
                 this directory will be listed.

    LIST       : Similar to DIR but shows filenames and descriptive
                 labels.

    TYPE file  : Displays the contents of any ASCII file. If you have
                 paging mode enabled then a request to continue or abort
                 will be sent after #n lines (as you have set with the
                 OP command in OPTIONS).

    GET file   : Downloads the contents of any ASCII file. The whole
                 file is transferred without any paging.

    PUT file   : Uploads any ASCII file from a user to the BBS.
                 The file must end with a ^Z  or \EX to be accepted.

    YGET file  : Download a binary file. YAPP protocol must be used.

    YPUT file  : Upload a binary file. YAPP protocol must be used.

    VIEW file  : Calls the external shareware utility FV.COM and prints
                 to screen a contents listing of the compressed archive.
                 For example, a user might see the file UTILS.ARJ and
                 be curious as to what the archive contains. By sending
                 the command VIEW UTILS the response will be:

                 Archive: C:\BINARY\GENERAL\UTILS.ARJ

                 Name        Length    Method   Size   Mod Date   CRC
                 ====        ======    ======   ====   ========   ===
                 DIAGS.COM    19759  Imploded   6916   02-Nov-91  1AE64E7B
                 VGATXT.EXE   32665  Imploded   9976   01-Jan-80  2EF44A6F
                 80387.EXE     8777   Stored    8777   23-Dec-91  9FAC9B06
                 ==========   =====  ========  ======  =========  ========
                 Total 3      61201  ZIP 1.01  25669   42%        
                    
                 Users can then determine if the contents of the archive
                 are desirable for download.

    EDIT file  : Activate the on-line file line editor. If the file
                 already exists, it must have been uploaded by the same 
                 user that requests to edit it. The available commands are:-

             ? : Shows all commands that can be used in the editor.

             A : Adds a line after the current line. The text for the
                 new line shall follow the letter A. If more commands are
                 to follow after the text, the text must end with a "/"
                 before the next command.  If the character "/" itself is 
                 to used in the text, the a "\" must be added before the "/".
 
                 If the "\" is to be used in the text as a valid character,
                 it must be specified twice ("\\"). Pointer will be at the 
                 start of the new line.

             B : Go to start of file.
             E : Go to end of file.

             F : Search for the first occurrence of a character (or string 
                 of characters) in the file. The search starts at the
                 current line. The string of characters must end with a 
                 "/" if more commands are chained (see the paragraph on 
                 the A-command).
       
            I : Insert a line before the current line.  Read about ending
                with a "/" in the paragraph on the A-command.

            K : Delete the number of lines that are stated just before the 
                letter K.   Example:  3K
                If no number is specified, then 1 line is deleted.
       
            L : Move a number of lines within the current line. The number
                can be negative to move towards the start of the file.
                Examples:  5L   -10L
       
            N : Toggle line-numbering on/off.

            P : Show a number of lines from the current line.  Example 8P.  
                This will show 8 text lines, starting with the current line.
       
            R : Search and replace.  Search for a string of characters and 
                replace it with a new one.  Example:  RALL/NONE  will 
                replace all ALL with NONE from the current line to the end 
                of the file.
        
            S : Save the edited file.
            Q : Exit the editor without saving the file.

      Examples: "EDIT>B5L10P" sets the pointer at the start of file.
                 Move 5 lines down, and  show 10 lines from there.
                     
                "EDIT>B4L6K-2L1OP" sets the pointer to the start of the 
                file. Move down 4 lines.  Delete 6 lines.  Move back 2 
                lines, and show 10 lines.
                     
                "EDIT>BFHello/K-2L5P" sets the pointer to the start of file,
                searches for "Hello", deletes the line containing "Hello",
                 moves back 2 lines and shows 5 lines.
                     
                "EDIT>BFHello/IThis is one new line with \/ so there/-1L3P"
                sets the pointer to start of the file. Searches for "Hello", 
                and inserts the new line.  The new line also contains the 
                character "/".  Goes back 1 line and shows 3 lines.
                     
                "EDIT>SQ"  saves the edited file and quits the editor.

    COPY Origin Destination : Copies the contents of one file into another
                              file. If the target file already exists, it
                              must "belong" to that user in order to
                              overwrite it.

                              Syntax: COPY THIS.TXT THAT.TXT

    DEL file   : Deletes a file provided that it "belongs" to that user.

   CD directory: Changes the active directory. The command allows you to  
                 move around withÿn the directory tree by changing the
                 active directory. "CD.." moves "upstream" by one directory.

   MD directory: Creates a new directory. The new directory is appended
                 below the current directory.

   RD directory: Deletes a directory. (Only if it is empty)

   EXIT        : Exits FBB-DOS and places the user back in mailbox mode.
   QUIT        : Exits FBB-DOS and places the user back in mailbox mode.




TELEPHONE MODEM CALLERS:
------------------------

GB7BBS is connected to the Public Switched Telephone Network, and can be 
called 24 hours per day on (0746).862531 locally or on +44.746.862531 from
overseas. The data format used is N81, speeds from 1200 through to 16800
bauds are accepted with either MNP or HST compression.

All callers to GB7BBS should be set to recive ANSI graphics where possible
and will see this opening colour screen as soon as they are connected:-

Û²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²Û
Û²²²²²²²²²²²²ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»²²²²²²²²²²Û
Û²²²²²²²²²²²²º                   G B 7 B B S                      º°²²²²²²²²²Û
Û²²²²²²²²²²²²ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹°²²²²²²²²²Û
Û²²²²²²²²²²²²º             FBB SysOp Support Mailbox              º°²²²²²²²²²Û
Û²²²²²²²²²²²²º                 Bridgnorth, England                º°²²²²²²²²²Û
Û²²²²²²²²²²²²ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹°²²²²²²²²²Û
Û²²²²²²²²²²²²º                   +44.746.862531                   º°²²²²²²²²²Û
Û²²²²²²²²²²²²ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°²²²²²²²²²Û
Û²²²²²²²²²²²² °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°²²²²²²²²²Û
Û²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²Û
Û²²ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿²²Û
Û²²³             US Robotics Dual Std Modem  (1200-16800 Baud)            ³°²Û
Û²²³             Non-Registered Users have 'READ-ONLY' access.            ³°²Û
Û²²ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ°²Û
Û²² °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°²Û
Û²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²Û

Callsign: 

From here on there are two modes of operation available.

- Read Only Access

If you are not a registered user of GB7BBS, when you enter your callsign you
will be advised that your are "not registered" and that you have READ ONLY 
status. This means that you have access most areas of the mailbox and server,
but you will be unable to either send messages (except to the SysOp) or to
upload files. This is to inhibit any unwanted disturbance to the Packet 
Network from unauthorised callers. 

You should leave a message addressed to SYSOP if you want to be authorised to
have a "full access", making sure to include your personal details along with
your desired password and the callsign of your HomeBBS where you can be 
contacted in case of query.

- Full access

If you have been authorised by the SysOp for modem access, and have been given
a password, then during log-on you will be asked for both your callsign and
your password. If your replies match the records in the user file then you 
will gain full access, just as if you had called in on one of the RF ports.
Full access is only required for those users who wish to either send mail
or upload files to GB7BBS, all other activities are available on the READ
ONLY access.

Download limits are identical for both levels of access status, and are
shown at the system prompt thus:-

GB7BBS User Files Area (v5.15b) 01.01.94
[Downloaded 128Kb] ...........This counter is reset nightly
[Authorised 500Kb]        
C:\

The following download protocols are supported by GB7BBS:-

   XMODEM    1K-XMODEM     1K-XMODEM-G
   YMODEM    YMODEM-G      YMODEM-BATCH
   ZMODEM
   
Full ZMODEM crash recovery and batch download functions are operational.
High speed connects of 14400+ should expect to see transfer speeds of
1600cps and above.

Uploads should be made using 'Vanilla' 128K XMODEM.



REMOTE SERVER COMMANDS:
-----------------------

All of these remote Servers are activated by sending normal text messages.
The message is received by the BBS and the instructions it contains
acted upon no later than one minute after receipt.
 
The result of the action (be it message creation, a file search, a file
request or a remote White Pages Query) is then generated into a message
addressed to you and placed into the mailbox for delivery.


AUTO7P Server
-------------

(FOR BINARY FILES)

Use the AUTO7P server to send messages to a BBS and receive a reply
which contains a particular binary file from the mailbox files area.

This file will be assembled into 7PLUS format and despatched to you in
5Kb sections. If the file is large the issue if these 7PLUS section files
will be restricted to a maximum of 4 messages per hour, to prevent Network
congestion.

You should previously establish the name and location of required file
using the REQDIR facility (see elsewhere).

The message format is as follows:-

Address      :   SP AUTO7P @ GB7BBS
Title        :   [DRIVE]\DIRECTORY\FILENAME @ GB7***
Message text :   ^Z 

The message title is most important as it contains all the information
required by the Server to carry out your request and return your message.

It can have different parameters specified, as shown in the following
examples.

The @ GB7*** in the title line informs the distant mailbox the callsign
of the mailbox to which you require your reply to be returned. This
field is optional, however, if it is not include dthen the message will
be returned to you addressed at the first BBS seen in the R: header lines 
of the received request.

You will not need to fully understand how directories and files are named 
according to DOS (Disc Operating System) conventions to use the 7PSERV
server. It should be sufficient to use the general rule of stating the
directory first followed by the file name and any extension.(Note filenames
are made up of two sections of up to eight and three characters each
separated by a point/period:

Example: USERDOCS.001 , USER.01 or USER01, are all acceptable)

Between the names of directories and/or the filenames is the "\" 
switch. This is the character which slants from right-to-left and 
should not be confused with the oblique (forward) slash "/". 

Address      :    SP AUTO7P @ GB7xxx
Title        :    FLTSIM\SCENERY\HEATHROW.ZIP  @ GB7***       
Message text :    ^Z

This message instructs the distant BBS to send you the file HEATHROW.ZIP
which resides on drive C: in the SCENERY directory, which is off the
FLTSIM area. 

The file will be assembled into a 7PLUS format, divided and returned to 
your home mailbox. Should you encounter decoding difficulties then just
send the Error Request back to the AUTO7P server at GB7BBS, making sure 
you address it to:

   SP AUTO7P @ GB7BBS

and a correction message will be generated and despatched automatically.

Where possible users are requested to consider the effect that numerous
AUTO7P requests could have on parts of the Packet Network that suffer from
poor links. It is therefore suggested that large numbers of file requests
are sent steadily, over a period of time, rather than in one single burst 
of activity.


FNDFIL Server
-------------

Use the FiNDFILe server to send a message to a suitably equipped Mailbox
and receive a reply message containing a listing of the files from a
specified directory which contain a certain keyword or group of words.

Use the REQDIR server to determine in which directory the target files
reside, and then send a message formatted as follows:-

Address      :   SP FNDFIL @ GB7$$$
Title        :   DRIVE\DIRECTORY\SEARCH STRING @ GB7***
Message text :   ^Z

The @ GB7*** in the title line informs the distant mailbox the callsign
of the mailbox to which you require your reply to be returned. This
field is optional, however, if it is not include dthen the message will
be returned to you addressed at the first BBS seen in the R: header lines 
of the received request.

Note: The "SEARCH STRING" is the collection of alpha-numeric characters
and spaces which will be searched for in the text of the files. Only
the filenames of those files which contain an EXACT match will be returned.

For example:

Address      :   SP FNDFIL @ GB7$$$
Title        :   D:\TNCTIPS\AM7910 MODEM CHIP @ GB7***
Message text :   ^Z

The Server will search all of the files which reside in the TNCTIPS
directory on drive D:\ and advise you of the name of any file which
contains the search string "AM7910 MODEM CHIP", it does not differentiate
between upper or lower case, but what it will not detect are occurrences
such as:

                 AM-7910 MODEM CHIP  } 
                 AM7910 M0DEM CHIP   }  Will not be acknowledged 
                 AM-7910 MODEM I.C   }

It is therefore advisable to keep the search string both short and unique.
For example by selecting the search string "7910" then the Server would
have parsed all the above examples as acceptable against the original
request.

Just like in the other Servers you can travel further along the DOS
tree and access files in sub-directories as the following example shows:-

Address      :   SP FNDFIL @ GB7$$$
Title        :   D:\TNCTIPS\PK80\MF10 FILTER @ GB7***
Message text :   ^Z

Once you have established which files contain the required search string,
they can be obtained using the REQuest FILe server detailed in the previous
section.



NEWDOC Server
-------------

The NEWDOC Server to add text files to the Library area of an FBB Mailbox.

The NEWDOC Server will accept input of any text file, store it into the 
designated area of the Library, add the appropriate label and update the 
main file index. The text file should be sent as a normal Server message
in the following format:-

Address      :   SP NEWDOC @ GB7$$$
Title        :   DIRECTORY\FILENAME File title up to 30 characters
Message text :   The file to be added to the library
End message  :   ^Z


The message title is most important as it contain all the information
required by the Server to carry out your request and file the text in
the correct topic area (directory). A space must be given after end of 
the filename and before your chosen title (up to 30 characters only).

If no title is added the Server action will be aborted.

To determine where the file should be placed first enter the Library
and check the available topic areas:-

From the main Mailbox menu type "F" to enter the Server:-

Server Menu 
----------- 
B: Bye
C: Connect Statistics
D: Library
F: Return to Mailbox
N: User Database
Q: QRA Finder
T: Satellit>s 
>

Select option "D" to access the Library and then "L" see the topic areas:-

1 COMPUTER          2 RECIPES         3 RIGMODS         4 TNCTIPS

Library Menu 
------------ 
B: Bye
F: Return to Sever Menu
L: View topics and/or filenames
#: The number that you wish to view

Library>

If the text file (which in this case has the name G3RUHMOD.9K6) is suitable
to be added to the TNCTIPS topic area then return to Mailbox mode and
send the message using the following format:-

Address      :   SP NEWDOC @ GB7$$$
Title        :   COMPUTER\G3RUHMOD.9K6 The G3RUH 9600 Baud Pkt Modem
Message text :   The text contents of the information file
End message  :   ^Z

Between the names of topics (directories) and/or the filenames is the "\" 
switch. This is the character which slants from right-to-left and should
not be confused with the oblique (forward) slash "/". 

If the Library contains more than one level of topic area (sub-directories)
as the following example:

1 COMPUTER          2=RECIPES          3 RIGMODS          4 TNCTIPS

Library Menu 
------------ 
B: Bye
F: Return to Sever Menu
L: View topics and/or filenames
#: The number that you wish to view

Library>

Select "2" to view the RECIPES topic:-

1 BEEF          2 CHICKEN          3 LAMB          4 PORK


Library Menu 
------------ 
B: Bye
F: Return to Sever Menu
L: View topics and/or filenames
#: The number that you wish to view

Library>

Then to add an information file called COQAUVIN.REC to the CHICKEN topic
area would require the NEWDOC Server message be addressed as follows:-


Address      :   SP NEWDOC @ GB7$$$
Title        :   RECIPES\CHICKEN\COQAUVIN.REC Traditional Coq Au Vin
Message text :   The text contents of the information file
End message  :   ^Z


Upon receipt of this message NEWDOC server will update the Library with
the file and return a message to the originator confirming the required
actions have been completed.

Note: 

Some FBB installations place restrictions on who can use the NEWDOC
Server, this is not the case at GB7BBS. Feel free to upload files if 
you so wish and create new topic areas if you feel it necessary.



REQDIR Server
-------------

To use the REQuest DIRectory server you send a message and receive a reply
which lists all the directories on the mailbox or alternatively the filenames
available within a specified  directory. You may then send a further request 
using the REQFIL message (described later) to obtain a copy of the file which 
will be automatically forwarded back to your home BBS.

The message format is as follows:-

Address      :   SP REQDIR @ GB7$$$
Title        :   DISK\DIRECTORY @ GB7***
Message text :   /EX or ^Z

Address the message as normal using the callsign GB7$$$ as the callsign
of the distant mailbox from where you wish the listing of either directories
or files to be obtained.

The message title is most important as it contain all the information
required by the Server to carry out your request and return your message.

It can have a number of different parameters specified as shown in the
following examples.

The @ GB7*** in the title line informs the distant mailbox the callsign
of the mailbox to which you require your reply to be returned. This
field is optional, however, if it is not include dthen the message will
be returned to you addressed at the first BBS seen in the R: header lines 
of the received request.

Title: D:\*.* @ GB7BBS       

This instructs the distant BBS to send a listing of all the directories and 
files, which exist on disk drive D: of the mailbox. Which may look like this:-


Msg # 62576   Type:P   Stat:R    To:G1DIL      From:GB7BBS  
Date: 01-Jan 00:01
Subject: Req Dir: *.*

Path Requested: D:\*.*

Disks available: C: D:

RECIPES         <DIR>   Gourmet recipes for Gastronauts
RIGMODS         <DIR>   1000's of mods for 100' of rigs 
TNCTIPS         <DIR>   Mods, Hints and tips for most TNCs
USERDOCS        <DIR>   Full user documentation files for BBS

[End of message # 62576]

Once this has been received then you can interrogate an individual 
directory to obtain a list of the files available. Here you must 
specify a directory name. For example :-

Title: D:\TNCTIPS @ GB7XYZ

In this example a list of all the files in the directory TNCTIPS which
is on drive D: will be made up into a message and sent to you at GB7XYZ,

the reply may look something like this:-

Msg # 62577   Type:P   Stat:R    To:G1DIL      From:GB7BBS  
Date: 01-Jan 00:02
Subject: Req Dir: D:\TNCTIPS

Path requested: D:\TNCTIPS

Disks available: C: D:

TINY2           <DIR>   This directory contains files on TINY2     
DL-4            <DIR>   Files relating to the MAXPAK DL-4 TNC
!INDEX             3K   Dynamic index file for this directory
AM7910.INF         4K   Info on the AM7910 World Modem chip
BSXDIAG.DCD        1K   Basic DCD layout for the BSX2 TNC
PK232-TS.440       2K   How to connect a PK232 to Trio TS440S 
TNC220.9K6         1K   Mods to run an old TNC220 at 9600 baud
      
[End of message # 62577]

If, on receipt of this message, you find that you wish to interrogate
another directory further down the tree structure, you should issue a 
request where the title input would be:-

Title: D:\TNCTIPS\TINY2\*.* @ GB7XYZ

Your subsequent reply would look something like this:-


Msg # 62578   Type:P   Stat:R    To:G1DIL      From:GB7BBS  
Date: 01-Jan 00:03
Subject: Req Dir: D:\TNCTIPS\TINY2

Path Requested: D:\TNCTIPS\TINY2\*.*

Disks available: C: D:


G3RUHMOD.001       1K      Modifications to the G3RUH modem Pt.1
G3RUHMOD.002       2K      Modifications to the G3RUH modem Pt.2
TINY2MOD.DOC       4K      Modifications to the PacComm TINY2
TINY2CW.ID         5K      Add hardware CW-ID to your Tiny 2
TINY2-CA.BLE       2K      Connections for hardware handshaking
      ÿ
[End of message # 62578]


You can see from the above message that there are no other Directories
shown, you are now at the end of the "branch" on this part of the DOS
tree. Now that you know the names of all the files you are ready to
request that one is sent to you. For this you will need to use the REQFIL
server.


REQFIL Server      
-------------

(ONLY FOR TEXT FILES)

Use the REQuest FILe server to send messages to a BBS and receive a reply
which contains a particular ascii text file from the mailbox files area.

You should previously establish the name and location of required file
using the REQDIR facility.

The message format is as follows:-

Address      :   SP REQFIL @ GB7$$$
Title        :   DRIVE\DIRECTORY\FILENAME @ GB7***
Message text :   ^Z 

The message title is important as it contains all of the information
required by the Server to carry out your request and return your message.

It can have different parameters specified, as shown in the following
examples.

The @ GB7*** in the title line informs the distant mailbox the callsign
of the mailbox to which you require your reply to be returned. This
field is optional, however, if it is not include dthen the message will
be returned to you addressed at the first BBS seen in the R: header lines 
of the received request.

You will not need to fully understand how directories and files are named 
according to DOS (Disc Operating System) conventions to use the REQFIL
server. It should be sufficient to use the?general rule of stating the
directory first followed by the file name and any extension.(Note filenames
are made up of two sections of up to eight and three characters each
separated by a point/period:

Example: USERDOCS.001 or USER.01 or USER01, all are acceptable)

Between the names of directories and/or the filenames is the "\" switch.
This is the character which slants from right-to-left and should not
be confused with the oblique (or forward) slash "/". 

Address      :    SP REQFIL @ GB7$$$
Title        :    D:\TNCTIPS\BSXDIAG.DCD  @ GB7***       
Message text :    ^Z

This message instructs the distant BBS to send you the file BSXDIAG.DCD
which resides on the D: drive, in the TNCTIPS directory. The file will
be assembled into a completely normal message and returned to your home
mailbox, or even to your PMS if you have auto-forwarding established.

To request a file which is in a sub-directory, off another directory
then the request would look like:-

Address      :    SP REQFIL @>GB7$$$
Title        :    D:\TNCTIPS\TINY2\TINY2-CA.BLE @ GB7***
Message Text :    ^Z
    
Where possible users are requested to consider the effect that numerous
REQFIL requests could have on parts of the Packet Network that suffer from
poor links. It is therefore suggested that large numbers of file requests
are sent steadily, over a period of time, rather than in one single
burst of activity.


REDIST - Message Re-distribution Server
---------------------------------------

This Server allows users to send a bulletin to everyone in a large city in 
Europe, or a state in America or the whole of Australia or any other Country
so avoiding the need to sendessages to 'ALL @ EU' or even worse, 'ALL @ WW' 
when trying to attract the attention of users in just a small area of Europe 
or the rest-of-the-world.

The REDIST server is addressed using four different names, depending on the
size of the area that you want the bulletin to cover.  The four server names
are LOCBBS, LOCAL, REGION and NATION.  If you want to send a bulletin only to
the remote BBS, then you would use the LOCBBS server.  To send a bulletin to
the few BBSs surrounding the remote BBS, then you would send a message to the
LOCAL server.  Similarly to address messages to a larger area around the BBS
you would use the REGION server and for the entire country that the BBS is in
you would use the NATION server.

All four servers are used in the same way.  In the following example, just
replace the 'LOCAL' with 'LOCBBS', 'REGION' or 'NATION' to use the other
servers.

Like all other Server messages, it is essential that your message is  sent
using 'SP' and not 'SB'.  If you use SB the server will NOT process your
request.

Address  :  SP LOCAL @ BBScall   <----or SP LOCBBS, SP REGION or SP NATION
Title    :  Test Message         <----Subject - put anything here
Msg Text :  Text of a test message to the LOCAL server at BBScall.
         :  /EX or CTRL-Z

When your message arrives at the BBS running the server it will be processed
and re-distributed as a bulletin to 'ALL @ xxxxxx' where 'xxxxxx' is the
translation the sysop of the remote BBS has chosen for LOCBBS, LOCAL, REGION
or NATION, depending on which server you used.

When the server has distributed your message a reply will be sent to you
confirming that the distribution has been completed successfully.  Remember
that this reply may take a few days to get back to you if the remote BBS is in
another country.

The server adds information to the copied bulletin that will allow anyone
reading your redistributed bulletin to use the 'SR' command to send a reply
to you.

- Special facilities

If you want to address your message to something other than 'ALL', then you
must add the relevant 'TO' field, preceded by the '#' character and
followed by a space, at the start of the subject line.  For example:

Address  :  SP REGION @ BBScall      <----or SP LOCBBS, SP LOCAL or SP NATION
Title    :  #50MHZ Test Message      <----Subject
Msg Text :  Text of a test message to the REGION server at BBScall.
         :  /EX or CTRL-Z


The above message would distribute a bulletin as 'SB 50MHZ @ xxxxxx' where
'xxxxxx' is whatever region is defined by the sysop @ BBScall.

NB.  You don't need to use the above format in the subject line.  If you omit
the information then your message will still be distributed to 'ALL @ xxxxxx'.
The remote sysop may choose not to use 'ALL'.  If not, your bulletin will be
sent out with some locally relevant TO field.

NB.  It is essential that you precede any change to the 'TO' field in the
subject line with the '#' character and put a space between the end of the
replacement TO field and the remainder of the subject line.  Replacement TO
fields can be up to 6 characters.



SCANBULL Message Scanning Server
--------------------------------

How often have you listed the last 24 hours worth (or more) of bulletins
(hundreds of them!) and seen 5k bulletins with such illuminating subject lines
as 'Disks' or 'New software'.  You sit there and toss a mental coin to decide
whether you think the bulletin will be of any interest.  What's the betting
that if you read it, the contents are a million miles away from anything of
interest to you.  If you don't read it a friend says a few days later 'did you
see that excellent bulletin from G9XYZ' and when you go looking for it, the
bulletin has gone.  Well help is now at hand!

The SCANBULL message title and keyword search server can be used by all the
users of the GB7BBS to locate bulletins which contain at least one of a list of
keywords chosen by the user.  The keyword list is callsign specific and is
stored in a database on the BBS.  The user has full facilities to maintain the
list of keywords.

At a fixed time each day (the BBS maintenance session...usually at 04:00), the
SCANBULL server examines all bulletins which have arrived since the previous
run for keywords selected by users.  The TO and SUBJECT fields and the entire
message text (excluding forwarding headers) are checked for keywords. A list of
bulletins matching the keywords is built for each user of the server and the
list is then sent as a message to the user concerned.  If the user has PMS
forwarding set up then the message will be forwarded to them.

Users with PMS's that accept forwarding from the BBS can then send a request to
a second part of the server which allows copies of the bulletins to be
forwarded to them.  The bulletin copies can either be in 'user' format (no
forwarding headers include) which is suitableÿfor TNC type PMS's, or 'BBS'
format (includes forwarding headers) for stations running full BBS software.
The 'BBS' format allows the user to send replies direct to the bulletin
originator using the SR or similar command.

The SCANBULL server comprises of various parts. REQSCN and REQBUL are two
servers which can be used remotely, ie messages from a PMS can be sent to them.
SCANADD, SCANDEL and SCANLIS are programs which can be invoked from the BBS
prompt to carry out similar actions to the REQSCN server.


- REQSCN server 
  ~~~~~~~~~~~~~

REQSCN is used to update the database which holds the list of keywords chosen
by the user.  The database can hold up to 64 keywords per user (this limit has
been imposed to keep the bulletin scan times to a reasonable length of time).
Keywords are limited to 16 or less characters.  If you try to add a keyword of
more than 16 characters, only the first 16 chars will be stored.  This isn't
actually too much of a problem...I can't think of many words that aren't unique
in the first 16 characters!

Be careful how you specify keywords.  Common words like 'THE', 'AN', etc will
be matched by virtually all bulletins, so aren't much use.  You can specify
keywords to match partial words, so DX will match DXcluster and DXCC, you can
use this to your benefit, but watch out for side effects of getting bulletins
listed that you didn't expect!  Punctuation, spaces and line breaks within a
word (it has been known!!) WILL confuse the scanner.  So IBM won't find I.B.Mÿ
or I B M in a bulletin.  I will try to improve on this in future versions.

REQSCN is used to modify the keywords in your list by addressing a message to
the server in the following way...

      SP REQSCN @ GB7BBS
      REQUEST              <----Subject - put anything here it's not used

      A word1 word2 word3  <----Adds word1/2/3 to the SCAN list
      D word2              <----Deletes word2 from the list
      ?                    <----Shows words in SCAN list
      /EX or CTRL-Z

The following command letters are available (as shown above) :

A - Adds keyword(s) to the database.  Any number of keywords can be added (up
    to 64) by a single 'A' command.  Place the keywords to be added on the same
    line as the 'A' command, eg 'A PC IBM COMPUTER' adds the words 'PC', 'IBM',
    'COMPUTER' to your keyword list.

D - Deletes keyword(s) from the database.  Any number of keywords can be
    deleted (up to 64) by a single 'D' command.    Place the keywords to be
    deleted on the same line as the 'D' command, eg 'D COMPUTER' deleted the
    keyword 'COMPUTER' from your keyword list.

? - Displays a list of all your keywords from the database.  This is useful to
    check that you have the correct set of keywords in the list.

Any number of keywords can be added or deleted (up to 64) by a single 'A' or
'D' command.  I'd suggest that you keep the lines to less than 80 characters
though!

The REQSCN server will send you a reply detailing the actions that it has
taken.  If you have used the '?' command, the reply will contain the list of
keywords you requested.


- SCANADD/SCANDEL/SCANLIS programs
  ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

These two programs can be run whilst you are logged in to the BBS that is
running the SCANBULL server, ie they are like BBS commands and can be run from
the BBS prompt.  SCANADD is used to add keywords to your personal list. SCANDEL
is used to delete words from your keyword list.  SCANLIS lists your keywords.
The commands are used in the following way:

SCANADD word1 word2 word3

This adds words word1/word2/word3 to your keyword list.

SCANDEL word1

This deletes the word word1 from your keyword list.

SCANLIS

This lists all the keywords stored in your keyword list.  No extra parameters
are required on the command line.

These programs are governed by the same ÿules as the REQSCN server, ie 64 words
maximum in your list, 16 chars per keyword and no more than 80 character lines.


- REQBUL server
  ~~~~~~~~~~~~~

REQBUL is used to request copies of selected bulletins to be sent to your PMS.
When the scanning program has run and sent you a list of the bulletins
containing your keywords, you can use REQBUL to obtain copies of the bulletins.
This is really only of use if the BBS forwards to your PMS.  Users of TNC based
PMS's will need to be careful about the size and number of bulletins requested,
otherwise you are likely to overflow the memory in your TNC!

To request a copy of a bulletin using REQBUL, send a message to the server in
the following way...

      SP REQBUL @ GB7BBS
      REQUEST              <----Subject - put anything here it's not used

      R nnnnn, nnnnn       <----Read messages nnnnn, nnnnn
      V nnnnn, nnnnn       <----Verbose read messages nnnnn, nnnnn
      /EX or CTRL-Z


The following command letters are avialable, as shown above:

R - Sends a copy of the message in 'user' format.  This is basically the same
    as you'd see if you used the 'R' command on the BBS.

V - Sends a copy of the message in 'BBS' format.  This is basically the same as
    you'd see if you used the 'V' command on the BBS.  This allows suitable PMS
    software to automatically re-address replies to the message to the correct
    BBS (using the forwarding headers).  Only use the 'V' command if you run
    proper BBS type software as a PMS.

Any number of bulletins can be requested by a single 'R' or 'V' command.  I'd
suggest that you keep the lines to less than 80 characters though!  The commas
between the message numbers are optional, you must include a space if you don't
use commas though.

Remember that the scanning program only scans bulletins which have arrived
since it was last run.  The scanner will normally run once per day, so you
messages arriving during the previous 24 hours will normally be found in your
list.  This means that if you add 'IBM' to your list, the scanning program will
NOT find messages containing IBM that arrived (normally) more than 24 hours
ago.

Finally, please be aware that this software only works with GB7BBS. You
CANNOT request database updates or request copies of bulletins from remote
BBSs.  Any replies will be sent to you on the BBS running the server.  This is
a deliberate attempt to keep the amount of network congestion caused by use of
this server to a minimum.  As all bulletins can usually be found on all BBSs,
then it seems pointless getting one BBS to send copies of bulletins to another
BBS that already has them.



OVERSEAS COUNTRY CODES USED IN PACKET RADIO
-------------------------------------------

AFGHANISTAN......... AFG                ALBANIA............. ALB   
ALGERIA............. DZA                AMERICAN SAMOA...... ASM   
ANDORRA............. AND                ANGOLA.............. AGO
ANTARCTICA.......... ATA                ANTIGUA............. ATG
ARGENTINA........... ARG                AUSTRALIA........... AUS  
AUSTRIA............. AUT                BAHAMAS............. BHS
BAHRAIN............. BHR                BANGLADESH.......... BGD
BARBADOS............ BRB                BELGIUM............. BEL   
BELIZE.............. BLZ                BENIN............... BEN
BERMUDA............. BMU                BHUTAN.............. BTN   
BOLIVIA............. BOL                BOTSWANA............ BWA   
BOUVET.............. BVT                BRAZIL.............. BRA
BR. VIRGIN ISL...... VGB                BRUNEI.............. BRN   
BULGARIA............ BGR                BURMA............... BUR   
BURUNDI............. BDI                BYELORUSSIA......... BYS
CAMEROON............ CMR                CANADA.............. CAN   
CANTON ISL.......... CTE                CAPE VERDE.......... CPV   
CAYMAN ISL.......... CYM                CHAD................ TCD
CENT.AFRICAN REP.... CAF                CHILE............... CHL   
CHINA...............ÿCHN                CHRISTMAS ISL....... CXR   
COCOS ISL........... CCK                COLUMBIA............ COL
COMOROS............. COM                CONGO............... COG   
COOK ISL............ COK                COSTA RICA.......... CRI   
CROATIA............. HVR                CUBA................ CUB   
CYPRUS.............. CYP                CZECHOSLOVAKIA...... TCH
DENMARK............. DNK                DJIBOUTI............ DJI
DOMINICAN REP....... DOM                DOMINICA............ DMA   
EAST TIMOR.......... TMP                ECUADOR............. ECU   
EGYPT............... EGY                EL SALVADOR......... SLV
EQUAT.GUINEA........ GNQ                ETHIOPIA............ ETH   
FAROE ISL........... FRO                FALKLAND ISL........ FLK   
FIJI................ FJI                FINLAND............. FIN
FRENCH POLYNESIA.... PYF                FRANCE.............. FRA   
FRENCH GUIANA....... GUF                GABON............... GAB   
GAMBIA.............. GMB                GERMANY............. DEU
GHANA............... GHA                GIBRALTAR........... GIB   
GREECE.............. GRC                GREENLAND........... GRL   
GRENADA............. GRD                GUADELOUPE.......... GLP
GUAM................ GUM                GUATEMALA........... GTM   
GUINEA.............. GIN                GUINEA-BISSAU....... GNB   
GUYANA.............. GUY                HAITI............... HTI
HEARD ISL........... HMD                HONDURAS............ HND   
HONG KONG........... HKG                HUNGARY............. HUN   
ICELAND............. ISL                INDIA............... IND
INDONESIA........... IDN                IRAN................ IRN   
IRAQ................ IRQ                IRELAND............. IRL   
ISRAEL.............. ISR                ITALY............... ITA
IVORY COAST......... CIV                JAMAICA............. JAM   
JAPAN............... JPN                JOHNSTON ISL........ JTN   
JORDAN.............. JOR                KAMPUCHEA........... KHM
KENYA............... KEN                KIRIBATI............ KIR   
NORTH KOREA......... PRK                SOUTH KOREA......... KOR   
KUWAIT.............. KWT                LAOS................ LAO
LEBANON............. LBN                LESOTHO............. LSO   
LIBERIA............. LBR                LIECHTENSTEIN....... LIE   
LIBYA............... LBY                LUXEMBOURG.......... LUX
MACAU............... MAC                MADAGASCAR.......... MDG   
MALAWI.............. MWI                MALAYSIA............ MYS   
MALDIVES............ MDV                MALI................ MLI
MALTA............... MLT                MARTINIQUE.......... MTQ   
MAURITANIA.......... MRT                MAURITIUS........... MUS   
MEXICO.............. MEX                MIDWAY ISL.......... MID
MONACO.............. MCO                MONGOLIA............ MNG   
MONTSERRAT.......... MSR                MOROCCO............. MAR   
MOZAMBIQUE.......... MOZ                NAMIBIA............. NAM
NETH.ANTILLES....... ANT                NAURU............... NRU   
NEPAL............... NPL                NEW CALEDONIA....... NCL   
NETHERLANDS......... NLD                NEW ZEALAND......... NZL
NICARAGUA........... NIC                NIGER............... NER   
NIGERIA............. NGA                NIUE................ NIU   
NORFOLK............. NFK                NORWAY.............. NOR
PACIFIC ISL......... PCI                OMAN................ OMN   
PAKISTAN............ PAK                PAPUA NEW GUINEA.... PNG   
PANAMA.............. PAN                PARAGUAY............ PRY
PITCAIRN ISL........ PCN                PERU................ PER   
PHILIPPINES......... PHL                POLAND.............. POL   
PORTUGAL............ PRT                PUERTO RICO......... PRI
QATAR............... QAT                REUNION ISL......... REU   
ROMANIA............. ROM                ST.KITTS NEVIS...... KNA   
RWANDA.............. RWA                ST. HELENA.......... SHN
ST.PIERRE & MIQ..... SPM                ST. LUCIA........... LCA   
SAN MARINO.......... SMR                ST.VINCENT & DEP.... VCT   
WEST. SAMOA......... WSM                SAO TOME............ STP
SAUDI ARABIA........ SAU                SENEGAL............. SEN   
SEYCHELLES.......... SYC                SIERRA LEONE........ SLE   
SINGAPORE........... SGP                SOLOMON ISL......... SLB
SOUTH AFRICA........ ZAF                SOMALIA............. SOM   
SPAIN............... ESP                SVALBARD JAN MAYEN.. SJM   
SRI LANKA........... LKA                SUDAN............... SDN
SURINAME............ SUR                SWAZILAND........... SWZ   
SWEDEN.............. SWE                SWITZERLAND......... CHE   
SYRIA............... SYR                TAIWAN.............. TWN
TANZANIA............ TZA                THAILAND............ THA   
TOGO................ TGO                TRINIDAD & TOBAGO... TTO   
TOKELAU............. TKL                TONGA............... TON
TURK AND CAICOS..... CAI                TUNISIA............. TUN   
TURKEY.............. TUR                TUVALU.............. TUV   
UGANDA.............. UGA                UKRAINE............. UKR
UNIT.ARAB EMIRATES.. ARE                UNITED KINGDOM...... GBR   
UNITED STATES....... USA                US PACIFIC ISL...... PUS   
US VIRGIN ISL....... VIR                URUGUAY............. URY
UPPER VOLTA......... HVO                VANUATA............. VUT
VATICAN............. VAT                VENEZUELA........... VEN   
VIETNAM............. VNM                WALLIS & FUTUNA..... WLF   
WAKE ISL............ WAK                WEST. SAHARA........ ESH
YEMEN............... YEM                ZAIRE............... ZAR
ZAMBIA.............. ZMB                ZIMBABWE............ ZWE



FINAL FLAG
----------

This file has been created in good faith, in the spirit of Amateur Radio.

It may well (and probably does) contain a number of errors. The author
accepts no responsibility for any errors or ommissions, but would ask
that he be advised by Packet mail to G1DIL @ GB7BBS.#28.GBR.EU so that
furture updates may have them corrected.

Vy 73 de Andy Witts - G1DIL  

*** EOF (01-Jan-94)