ÍÍÍÍÍÍÍÍÍÍ[  USER GUIDE FOR TheNet X-1J ]Í
 Commando's - For users of TheNet X-1J Nodes

@Which commands are avaiable ?
This brief note is intended for users of TheNet X-1J, and explains the
basic commands. Configuration and sysop features are not covered fully.

TheNet  X-1J  is  an extension of TheNet 1, and provides a number of
new features.

The switch provides the following user commands :

          Connect
          Info
          Nodes
          Routes
          Users
          Talk
          CQ
          BBS
          Host
          MHeard
          Bye
          DXcluster
          IProute
          ARP
          QUIT

Not  all commands may be available on every node as certain commands
might have been disabled. If a command has been enabled, it will be
displayed when you  type  an  invalid command such as '?'. In addition,
there  are  some commands that are available but are not displayed.
The main ones of interest are :

          Links
          Stats
          IPAddress

@Connect

   If  the  connect command is given on its own, then  assuming  that  the
   sysop has set it up correctly, you will get connected to the local BBS.
   If you give another callsign, either of a local station or a node,  the
   node  will attempt to connect you to that station either by a  level  4
   connection  or  by downlinking. If you are downlinking,  you  may  also
   specify digipeaters.

   In either case, you get either a connected message or a message telling
   you  of the failure to connect. If you enter any other command at  this
   stage, the connection attempt will be aborted.

   If you attempt to downlink with digipeating, or attempt to downlink  to
   an  invalid callsign such as a node alias with an SSID, you may get  an
   error message depending on how the Sysop has configured the node.

   Finally,  if you connect to the node, then connect to another  station,
   and  that station disconnects you ( e.g. connect to a BBS and  use  the
   'Bye'  command of the BBS, you will either get reconnected to the  node
   or disconnected completely depending on the configuration of the node.

   If  you  enter a node alias and get an 'invalid call' message,  it  can
   either  be because the node is not recognised or it can be because  the
   Sysop has made node aliases case sensitive.



@Info

   This  command  gives information about the node as a combination  of  a
   message stored in the EPROM and a message entered by the Sysop.

@Nodes

   This  command gives information about the distant nodes that this  node
   thinks  it  can  get  to. With no parameter, it  shows  the  alias  and
   callsign of all the nodes except those staring with a '#' character. If
   a parameter of '*' is given, those 'hidden' nodes will also be shown.

   If  a callsign or alias is given that the node does not know, it  gives
   an  error message. If the callsign or alias of a known node  is  given,
   the  node gives details of the routes it knows about that lead to  that
   destination.  The  display  shows one option per line,  each  of  which
   consists  of the path quality, obsolescence count and port followed  by
   the  callsign  of the neighbour. If any route is in use, a  chevron  is
   shown against the appropriate entry.

   If  so  configured  by the Sysop, 'Slime  trails'  i.e.  nodes  without
   aliases  that have not been the subject of a valid node broadcast,  may
   be omitted from the nodes list.

@Routes

   This command gives information about the neighbouring nodes that can be
   heard.  For  each  neighbour, the display shows the  port  number,  the
   callsign,  the path quality and the number of nodes accessible  through
   this  neighbour. If a route has been 'locked' by the sysop, then a  '!'
   character  is shown after an entry. The sysop may have  configured  the
   node  to  display  nodes  as  callsign  or  as  alias:callsign.  If  so
   configured,  then if a node is shown as a callsign alone it means  that
   is  it  not currently reachable as its node broadcasts  are  not  being
   received.

@Users

   This shows who is using the node. It does not show other nodes that are
   using  the  node as a level 3 relay, nor does it show those  users  who
   have connected to the node but otherwise have done nothing.

   The display shows the through connections, followed by those users  who
   are  connected to the switch and 'idle'. It also shows those users  who
   are  connected  to the conferencing facility. The latter  stations  are
   shown  connected to a destination called 'Talk', whilst in the case  of
   connections, the two endpoints are shown. For connections, two  symbols
   are  used,  '<-->'  and  '<..>'. The former  is  used  for  established
   connections   whilst   the  latter  is  used  for   connections   being
   established.

@Talk

   The Talk command allows a group of users to hold a conference call.  It
   also  allows  a  user to send a message to another  user  of  the  node
   provided  that  user  is connected to the switch  but  is  not  patched
   through  to another station and is not currently trying to  connect  to
   another station.
   A user enters the conference by giving the command 'talk'. He/she  gets
   a message informing them of this and reminding them that the command to
   escape  from the talk command is '/exit'. Any other users currently  in
   the conference get a message from the node telling them of the callsign
   of  the user who has joined them. At this point, every line sent  by  a
   user in the conference is copied to all other users in the  conference,
   preceded by their callsign.

   To exit from the conference, the command '/exit' is used. This causes a
   response  message to be sent to the user, and at the same time  all  of
   those  left in the conference get a message from the node telling  them
   of the station who has left the conference. If you force a  disconnect,
   the other stations are not told of your departure.

   A  string of text may be entered on the same line as the  talk  command
   when  the  command  is  given. If this is  done,  before  the  user  is
   connected  to  the conference, that string of text is sent to  all  the
   other  users  of  the node who appear in the 'user' list  but  are  not
   connected to anything else. For example if GxABC were to type :
              TALK GyXYZ, Hello fred can I have a chat - type TALK

   then other users of the node ( including presumably Fred, would get the
   message :

          GxABC>> GyXYZ. Hello fred can I have a chat - type TALK

   on  their  screens. The only exception to this is that sysops  are  not
   sent the message.

   Note that the TALK command will pass 8 bit data if set to by the Sysop.

@CQ

   This  command is used to broadcast a CQ message. In addition, the  fact
   that  you  are calling CQ is indicated in the USER list.  The  callsign
   will be your own with a different SSID, and anyone else can connect  to
   you by connecting to the callsign with the appropriate SSID.

   The CQ remains 'primed' for a while, and if any other command is  given
   to the node the CQ will be cancelled.

@BBS

   When you issue the BBS command, assuming that the sysop has  configured
   it, you will be connected to the local BBS.

   If  you enter the command 'BBS ?', then the current setting of the  BBS
   will be displayed.

@Host

   The  HOST command operates just like the BBS command. It may have  been
   disabled  by  the sysop, it may have been set to connect  to  the  same
   station as the BBS, or it may have been set to connect to another  host
   system.

   If you enter the command 'HOST ?', then the current setting of the HOST
   will be displayed.

@MHeard

   If  enabled,  the  heard list shows the last few  stations  heard.  The
   number  of entries is limited and set by the sysop so any stations  not
   heard  for  a  while may get pushed out of the list  by  others  heard.
   Assuming  that a station is not pushed out in this manner, the  display
   shows  the number of packets heard from that station since it  appeared
   in  the list and the time since it was last heard. The time  is  hours,
   minutes and seconds. The list also shows the port on which the  station
   was  heard ( port 0 is the radio port ), and if it hears IP  frames  or
   Net/Rom  frames,  it  adds a note to show that the station  is  a  node
   and/or a TCP/IP station.

   If the list is long enough so that a station is not heard for 12 hours,
   it will get deleted anyway.

   The  list  may  also show a column headed 'Dev.'.  This  will  only  be
   present  where the sysop has added to the node a small hardware  add-on
   that  measures the received signal audio level. Specifically, it  gives
   an  indication  of  the  peak  audio level.  By  means  of  a  software
   configuration  control and prior calibration, this gets converted  into
   an  indication of the transmitting station's signal deviation. It  does
   this by sampling the audio level after every valid packet.

   Care  must  be  taken  over its interpretation.  It  does  not  measure
   independently  the two tone levels - it is assumed that whatever  local
   standards that relate to pre-emphasis ( i.e. use it or not ) have  been
   implemented.

   Often, packet stations are set up, and the audio level tweaked until it
   appears to work reasonably error free. The idea of this add-on is that,
   having  done that, you then connect to the node and display  the  heard
   list to see an indication of your actual deviation. It may then be fine
   tuned to set it correctly. Local advice must be taken over the  correct
   setting as it depends on the channel spacing being used ( e.g. 12.5, 25
   or other KHz ).

   The meter will give the wrong answer on the following conditions :

        A badly distorted audio signal
        Badly off frequency
        Incorrect adherence to local pre-emphasis standards
        A very noisy signal

   If you connect, then correct your deviation to the correct display then
   find  performance  has  deteriorated, it indicates  one  of  the  above
   problems. It is not that the meter doesn't work, it is an indication of
   a fault elsewhere.

   It  is  in your own interest for those around you to  use  the  correct
   deviation. The list also allows you to see the deviation of others - so
   apply  peer pressure if someone over or under deviates. Remember it  is
   NOT  a  case of the higher or the lower the better - it is  having  the
   setting RIGHT.

   The system may also be used to migrate users towards a lower  deviation
   in advance of moving to narrower channel spacing.

@Links

   The  LINKS command shows the level 2 connections to the node.  This  is
   usually  of  academic interest, but I use it in  testing.  The  display
   shows the links, one per line, with the two callsigns, the link  state,
   the port number and the current number of retries.

@Bye and Quit

   These commands disconnects you from the node, closing the link. It says
   goodbye  before disconnecting you if it has been so configured  by  the
   sysop. Quit does just the same as Bye does.

@DXcluster

   If there is a local DXcluster, this command may have been configured by
   the sysop to connect you to it. It therefore operates in a manner  very
   similar to the BBS command.

@Stats

   The  stats command gives lots of data about the node operation. A  full
   description of the information is contained in the overview document.

@IProute

   This  command is used by the sysop to configure the IP route table.  It
   may also be used to display the router table.

@Arp

   This  command  is  similar to the IProute command, but  shows  the  Arp
   table.  The  Arp  table  provides a  translation  from  Ip  address  to
   callsign.

@IPaddress

   This command is used to display the current node IP address.